## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
wireless local loop (WLL)
education for life www.rimt.ac.in

## Slide 3: Definition
What is WLL?
- WLL is a system that connects subscribers to the local telephone station wirelessly.
Systems WLL is based on:
  Cellular
  Satellite (specific and adjunct)
  Microcellular
Other names
  Radio In The Loop (RITL)
  Fixed-Radio Access (FRA).
education for life www.rimt.ac.in

## Slide 4: A general WLL setup
education for life www.rimt.ac.in

## Slide 5: WLL services
Desirable:
  Wireless feature should be transparent
  Wireline Custom features
Other:
  Business related
    Hunt groups,
    Call transfers
    Conference calling
  Calling cards, coin phones
  V.29 (9600bps)
  ISDN (64kbps)
education for life www.rimt.ac.in

## Slide 6: WLL should provide…
Toll-quality service
Expand from a central office to about 5 miles
Low license cost
Subscriber costs equivalent or better than copper
education for life www.rimt.ac.in

## Slide 7: Ideas for U.S. market
Supplement Copper Lines
  Easier third telephone line
  Data service
Fixed Mobile Users
  Take phone wherever you want / charged on 2 levels
  “home” could mean neighborhood
  Charged regular mobile rate if you’re on the road
education for life www.rimt.ac.in

## Slide 8: Cost Considerations
Wireless cost is constant over distance for WLL
Wireline depends on distance AND terrain
education for life www.rimt.ac.in

## Slide 9: Situations “made” for WLL
Environments where 3rd line is degraded might be cheaper to go wireless
Where it’s impossible to lay copper (3rd world, small islands)
Business parks, industrial areas
Speedy deployment, stop gap application till wireline is in
  90-120 days for activation
education for life www.rimt.ac.in

## Slide 10: Developed vs. Developing
Developed: Wireline service
  Firmly established, cellular penetration is relatively high
  Incumbent operator would use it to install 2nd, 3rd lines, coverage to rural areas
  2nd or 3rd competitive operator deploy it for fast & cost effective deployment
  Quick way to establish market presence
  cellular complement to their offerings
education for life www.rimt.ac.in

## Slide 11: Developed vs. Developing
Developing
  Quick & easy to deploy in countries with little copper line service, so as to accommodate people on enormous waiting lists for basic service
  Low maintenance costs
  Allows more competition in provider market
education for life www.rimt.ac.in

## Slide 12: Examples
UK
  150 PTOs have licenses for wireless
  Focus on regional networks
  WLL Commercial services
    Ionica, Atlantic Telecom, Scottish Telecom
Poland
  Most exciting market in eastern Europe
  Local loop is the bottleneck
  150,000 WLL lines since 1996 (15% of new)
  Ericsson, Motorola contracts
education for life www.rimt.ac.in

## Slide 13: Connection Setup
PSTN
Switch
function
WLL
Controller
AM
HLR
Transceiver
WASU
Trunk
Air
Interface
UWLL
TWLL
Wireless Access Network Unit(WANU)
  Interface between underlying telephone network and wireless link
  consists of
    Base Station Transceivers (BTS)
    Radio Controller(RPCU)
    Access Manager(AM)
    Home Location Register(HLR)
WANU
Wireless Access Subscriber Unit(WASU)
  located at the subscriber
  translates wireless link into a traditional telephone connection
education for life www.rimt.ac.in

## Slide 14: Important Results of Fixed to Fixed Propagation in WLLs
Signal channel is not a Rayleigh fading channel:
  Power control algorithms are simpler and can be utilized more effectively
Channel Randomness is lost:
  Makes analysis difficult
Pathloss exponent is considerably smaller (Why?):
  20dB/dec compared to 40dB/dec
  Decreases cell capacity
  Allows for larger coverage area
education for life www.rimt.ac.in

## Slide 15: Fixed to Fixed Propagation(cont’d)
No handoffs necessary:
  Decreases hardware costs and system complexity
  Increases quality of service through accurate traffic predictions
Allows usage of directional antennas:
  Can greatly reduce interference and increase cell capacity
-30dB
30dB
0o
60o
-40dB
10dB
0o
120o
180o
BS antenna
Subscriber antenna
education for life www.rimt.ac.in

## Slide 16: In-Cell Interference (CDMA)
I = (Nh – 1)aS  NhaS
    a = voice activity factor
  Nh = total # of houses
    S = power received at cell site from every house
education for life www.rimt.ac.in

## Slide 17: Out-of-Cell Interference
Pathloss: 20dB/dec as opposed to 40dB/dec
 need to take in account more tiers
Only from houses whose antennas are directed at the center cell base station
education for life www.rimt.ac.in

## Slide 18: Interference from Another Cell
Blue area is region of interferers for C
It is Not a perfect pie shape
If w = (1/2)*(antenna width)
(in radians)
W = w+2sin-1((R/D)sin(w/2))
If w<<1 and R<<D:
W = w (1+(R/D))
is the “pie” arc length
education for life www.rimt.ac.in

## Slide 19: Per-Tier Interference
Integration over W and all the cells at tier n yields:
  In = [aNhSw/(3sqrt(3))][1/n]
  for n>4
Interference is proportional to antenna width w and inversely proportional to the tier number.
Decreasing the antenna width can greatly reduce interference.
As the number of tiers approaches infinity, so does the total interference. Therefore, system capacity is a function of the total number of tiers in the system.
education for life www.rimt.ac.in

## Slide 20: Capacity comparison for 5 MHz spectrum allocation
Detail | IS-95 CDMA |  | IS-136 TDMA |  | ETSI (GSM) | 
 | Mobile | WLL | Mobile | WLL | Mobile | WLL
Chan. BW (kHz) | 1250 | 1250 | 30 | 30 | 200 | 200
# channels | 4 | 4 | 167 | 167 | 25 | 25
Eb/N0 | 7 dB | 6dB | 18dB | 14dB | 12dB | 12dB
Freq. Reuse | 1 | 1 | 7 | 4 | 3 | 3
Effective Chan. Per sect. | 4 | 4 | 7.95 | 13.92 | 2.78 | 2.78
Erlangs per cell Per MHz | 38.3 | 48.7 | 9.84 | 19.6 | 9.12 | 9.12
education for life www.rimt.ac.in

## Slide 21: Comparison
WLL | Mobile Wireless | Wireline
Good LOS component | Mainly diffuse components | No diffuse components
Rician fading | Rayleigh fading | No fading
Narrowbeam directed antennas | Omnidirectional antennas | Expensive wires
High Channel reuse | Less Channel reuse | Reuse Limited by wiring
Simple design, constant channel | Expensive DSPs, power control | Expensive to build and maintain
Low in-premises mobility only, easy access | High mobility allowed, easy access | Low in-premises mobility, wiring of distant areas cumbersome
Weather conditions effects | Not very reliable | Very reliable
education for life www.rimt.ac.in

## Slide 22: Examples of services provided
Marconi WipLL (wireless IP local loop)
  Based on Frequency hopping CDMA
  Internet Protocol 64kbps to 2.4Mbps rates Committed Information Rate or best effort service
Lucent WSS (wireless subscriber system)
  800 to 5000 subscribers per switch
  Uses FDMA/FDD 12 Km to 40Km coverage
GoodWin WLL
  DECT standards
  9.6 kbps rate
  Specified conditions -5°С...+55°С, 20...75% humidity
education for life www.rimt.ac.in

## Slide 23: Future of WLL / Overview
Depends on
  economic development
  existing infrastructure of a region
Offers
  market competition
  quick deployment
  relatively reliable service at low costs
education for life www.rimt.ac.in

## Slide 24: Topics to be covered in next lecture
Local Multipoint Distribution System (LMDS)
education for life www.rimt.ac.in