## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
Wireless local Area Networks (WLANs)
education for life www.rimt.ac.in

## Slide 3: LAN/WLAN World
LANs provide connectivity for interconnecting computing resources at the local levels of an organization
Wired LANs
    Limitations because of physical, hard-wired infrastructure
Wireless LANs provide
    Flexibility
    Portability
    Mobility
    Ease of Installation
education for life www.rimt.ac.in

## Slide 4: Wireless LAN Applications
Medical Professionals
Education
Temporary Situations
Airlines
Security Staff
Emergency Centers
education for life www.rimt.ac.in

## Slide 5: IEEE 802.11 Wireless LAN Standard
In response to lacking standards, IEEE developed the first internationally recognized wireless LAN standard – IEEE 802.11
IEEE published 802.11 in 1997, after seven years of work
Most prominent specification for WLANs
Scope of IEEE 802.11 is limited to Physical and Data Link Layers.
education for life www.rimt.ac.in

## Slide 6: Benefits of 802.11 Standard
Appliance Interoperability
Fast Product Development
Stable Future Migration
Price Reductions
The 802.11 standard takes into account the following significant differences between wireless and wired LANs:
    Power Management
    Security
    Bandwidth
education for life www.rimt.ac.in

## Slide 7: IEEE 802 LAN Standards Family
IEEE 802.3
Carrier
Sense
IEEE 802.4
Token
Bus
IEEE 802.5
Token
Ring
IEEE 802.11
Wireless
IEEE 802.2
Logical Link Control (LLC)
PHY
OSI Layer 1
(Physical)
Mac
OSI Layer 2
(Data Link)
education for life www.rimt.ac.in

## Slide 8: IEEE 802.11 Terminology
Access point (AP): A station that provides access to the DS.
Basic service set (BSS): A set of stations controlled by a single AP.
Distribution system (DS): A system used to interconnect a set of BSSs to create an ESS.
  DS is implementation-independent. It can be a wired 802.3 Ethernet LAN, 802.4 token bus, 802.5 token ring or another 802.11 medium.
Extended service set (ESS):Two or more BSS interconnected by DS
Portal: Logical entity where 802.11 network integrates with a non 802.11 network.
education for life www.rimt.ac.in

## Slide 9: WLAN Topology Ad-Hoc Network
education for life www.rimt.ac.in

## Slide 10
WLAN Topology
Infrastructure
education for life www.rimt.ac.in

## Slide 11: IEEE 802.11 Services: Distribution of Messages
Distribution service (DS)
  Used to exchange MAC frames from station in one BSS to station in another BSS
Integration service
  Transfer of data between station on IEEE 802.11 LAN and station on integrated IEEE 802.x LAN
education for life www.rimt.ac.in

## Slide 12: Association Related Services
Association
  Establishes initial association between station and AP
Re-association
  Enables transfer of association from one AP to another, allowing station to move from one BSS to another
Disassociation
  Association termination notice from station or AP
education for life www.rimt.ac.in

## Slide 13: Access and Privacy Services
Authentication
  Establishes identity of stations to each other
De-authentication
  Invoked when existing authentication is terminated
Privacy
  Prevents message contents from being read by unintended recipient
education for life www.rimt.ac.in

## Slide 14: Reliable Data Delivery
Loss of frames due to noise, interference, and propagation effects
Frame exchange protocol
  Source station transmits data
  Destination responds with acknowledgment (ACK)
  If source doesn’t receive ACK, it retransmits frame
Four frame exchange for enhanced reliability
  Source issues request to send (RTS)
  Destination responds with clear to send (CTS)
  Source transmits data
  Destination responds with ACK
education for life www.rimt.ac.in

## Slide 15: Access Control
Distributed Coordination Function (DCF)
  Distributed access protocol
  Contention-Based
  Makes use of CSMA/CA rather than CSMA/CD
  Suited for ad hoc network and ordinary asynchronous traffic
Point Coordination Function (PCF)
  Alternative access method on top of DCF
  Centralized access protocol
  Contention-Free
  Works like polling
  Suited for time bound services like voice or multimedia
education for life www.rimt.ac.in

## Slide 16: CSMA/CD vs. CSMA/CA
CSMA/CD – CSMA/Collision detection
  For wire communication
  No control BEFORE transmission
  Generates collisions
  Collision Detection-How?
CSMA/CA – CSMA/Collision Avoidance
  For wireless communication
  Collision avoidance BEFORE transmission
  Why avoidance on wireless?
  Difference in energy/power for transmit & receive
  Difficult to distinguish between incoming weak signals, noise, and effects of own transmission
education for life www.rimt.ac.in
Notes: DIFS= Distributed interframe Space
PIFS=Point Coordination Interframe Space
SIFS=Short Coordination Interframe Space

## Slide 17: RTS-CTS-DATA-ACK
DIFS: Distributed IFS
RTS: Request To Send SIFS: Short IFS CTS: Clear To Send ACK: Acknowledgement
NAV: Network Allocation Vector
DCF: Distributed Coordination Function
education for life www.rimt.ac.in

## Slide 18: MAC Frame Format
Frame
Control
Duration
ID
Addr 1
Addr 2
Addr 3
Addr 4
Sequence
Control
CRC
Frame
Body
2
2
6
6
6
6
2
0-2312
4
802.11 MAC Header
Protocol
Version
Type
SubType
To
DS
Retry
Pwr
Mgt
More
Data
WEP
Order
Frame Control Field
Bits: 2
2
4
1
1
1
1
1
1
1
1
DS
From
More
Frag
education for life www.rimt.ac.in

## Slide 19: MAC Layer Frames
Data Frames
Control Frames
    RTS,CTS,ACK and PS-POLL
Management Frames
  Authentication and De-Authentication
  Association, Re-Association, and Disassociation
  Beacon and Probe frames
education for life www.rimt.ac.in

## Slide 20: IEEE 802.11 Security
Authentication provided by open system or shared key authentication (Authentication is used instead of wired media physical connection)
Privacy provided by WEP (Privacy is used to provide the confidential aspects of closed wired media)
An Integrity check is performed using a 32-bit CRC
education for life www.rimt.ac.in

## Slide 21: Authentication
education for life www.rimt.ac.in

## Slide 22: Is WLAN Secure ?
The Parking Lot attack
Man in the middle attack
Freely available tools like Air Snort, WEP crack to snoop into a WLAN
education for life www.rimt.ac.in

## Slide 23: Future of WLAN
WLANs move to maturity
  Higher Speeds
  Improved Security
  Seamless end-to-end protocols
  Better Error control
  Long distances
  New vendors
  Better interoperability
  Global networking
  Anywhere, anytime,any-form connectivity…
education for life www.rimt.ac.in

## Slide 24: Topics to be covered in next lecture
Bluetooth and Personal Area Networks
education for life www.rimt.ac.in