## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
Introduction to wireless system design
education for life www.rimt.ac.in

## Slide 3: Design Challenges
Wireless channels are a difficult and capacity-limited broadcast communications medium
Traffic patterns, user locations, and network conditions are constantly changing
Applications are heterogeneous with hard constraints that must be met by the network
Energy and delay constraints change design principles across all layers of the protocol stack
education for life www.rimt.ac.in

## Slide 4: Evolution of Current Systems
Wireless systems today
  2G Cellular: ~30-70 Kbps.
  WLANs: ~10 Mbps.
Next Generation
  3G Cellular: ~300 Kbps.
  WLANs: ~70 Mbps.
Technology Enhancements
  Hardware: Better batteries, Better circuits/processors.
  Link: Antennas, modulation, coding, adaptivity, DSP, BW.
  Network: Dynamic resource allocation, Mobility support.
  Application: Soft and adaptive QoS.
education for life www.rimt.ac.in

## Slide 5: Future Generations
Rate
Mobility
2G
3G
4G
802.11b WLAN
2G Cellular
Other Tradeoffs:
Rate vs. Coverage
Rate vs. Delay
Rate vs. Cost
Rate vs. Energy
Fundamental Design Breakthroughs Needed
education for life www.rimt.ac.in
Notes: -Diminishing returns by beating on the same areas for optimization
-Other network tradeoffs not even considered
-Fundamental breakthroughs both in the way wireless networks are designed and in the design tradeoffs that are considered.

## Slide 6: Quality-of-Service (QoS)
QoS refers to the requirements associated with a given application, typically rate and delay requirements.
It is hard to make a one-size-fits all network that supports requirements of different applications.
Wired networks often use this approach with poor results, and they have much higher data rates and better reliability than wireless.
QoS for all applications requires a cross-layer design approach.
education for life www.rimt.ac.in

## Slide 7: Crosslayer Design
Application
Network
Access
Link
Hardware
Delay Constraints
Rate Constraints
Energy Constraints
Adapt across design layers
Reduce uncertainty through scheduling
Provide robustness via diversity
education for life www.rimt.ac.in

## Slide 8: Crosslayer Techniques
Adaptive techniques
  Link, MAC, network, and application adaptation
  Resource management and allocation (power control)
Diversity techniques
  Link diversity (antennas, channels, etc.)
  Access diversity
  Route diversity
  Application diversity
  Content location/server diversity
Scheduling
  Application scheduling/data prioritization
  Resource reservation
  Access scheduling
education for life www.rimt.ac.in

## Slide 9: Current Wireless Systems
Cellular Systems
Wireless LANs
Satellite Systems
Paging Systems
Bluetooth
Ultrawideband radios
Zigbee radios
education for life www.rimt.ac.in

## Slide 10: Cellular Systems: Reuse channels to maximize capacity
Geographic region divided into cells
Frequencies/timeslots/codes reused at spatially-separated locations.
Co-channel interference between same color cells.
Base stations/MTSOs coordinate handoff and control functions
Shrinking cell size increases capacity, as well as networking burden
BASE
STATION
MTSO
education for life www.rimt.ac.in

## Slide 11: Cellular Phone Networks
BS
BS
MTSO
PSTN
MTSO
BS
San Francisco
New York
Internet
education for life www.rimt.ac.in

## Slide 12: 3G Cellular Design: Voice and Data
Data is bursty, whereas voice is continuous
  Typically require different access and routing strategies
3G “widens the data pipe”:
  384 Kbps.
  Standard based on wideband CDMA
  Packet-based switching for both voice and data
3G cellular struggling in Europe and Asia
Evolution of existing systems (2.5G,2.6798G):
    GSM+EDGE
    IS-95(CDMA)+HDR
    100 Kbps may be enough
What is beyond 3G?
The trillion dollar question
education for life www.rimt.ac.in

## Slide 13
Wireless Local Area Networks (WLANs)
WLANs connect “local” computers (100m range)
Breaks data into packets
Channel access is shared (random access)
Backbone Internet provides best-effort service
  Poor performance in some apps (e.g. video)
01011011
Internet
Access
Point
0101
1011
education for life www.rimt.ac.in

## Slide 14: Wireless LAN Standards
802.11b (Current Generation)
  Standard for 2.4GHz ISM band (80 MHz)
  Frequency hopped spread spectrum
  1.6-10 Mbps, 500 ft range
802.11a (Emerging Generation)
  Standard for 5GHz NII band (300 MHz)
  OFDM with time division
  20-70 Mbps, variable range
  Similar to HiperLAN in Europe
802.11g (New Standard)
  Standard in 2.4 GHz and 5 GHz bands
  OFDM
  Speeds up to 54 Mbps
Many WLAN
cards support
all 3
standards
education for life www.rimt.ac.in

## Slide 15: Satellite Systems
Cover very large areas
Different orbit heights
  GEOs (39000 Km) versus LEOs (2000 Km)
Optimized for one-way transmission
  Radio and movie broadcasting
Most two-way systems struggling or bankrupt
  Expensive alternative to terrestrial system
  A few ambitious systems on the horizon
education for life www.rimt.ac.in

## Slide 16: Paging Systems
Broad coverage for short messaging
Message broadcast from all base stations
Simple terminals
Optimized for 1-way transmission
Answer-back hard
Overtaken by cellular
education for life www.rimt.ac.in

## Slide 17: Bluetooth
8C32810.61-Cimini-7/98
Cable replacement RF technology (low cost)
Short range (10m, extendable to 100m)
2.4 GHz band (crowded)
1 Data (700 Kbps) and 3 voice channels
Widely supported by telecommunications, PC, and consumer electronics companies
education for life www.rimt.ac.in

## Slide 18: Ultrawideband Radio (UWB)
UWB is an impulse radio: sends pulses of tens of picoseconds(10-12) to nanoseconds (10-9)
Duty cycle of only a fraction of a percent
A carrier is not necessarily needed
Uses a lot of bandwidth (GHz)
Low probability of detection
Excellent ranging capability
Multipath highly resolvable
  Can use OFDM to get around multipath problem.
education for life www.rimt.ac.in

## Slide 19: Why is UWB Interesting?
Unique Location and Positioning properties
  1 cm accuracy possible
Low Power CMOS transmitters
  100 times lower than Bluetooth for same range/data rate
Very high data rates possible
  500 Mbps at ≈10 feet under current regulations
7.5 Ghz of “free spectrum” in the U.S.
  FCC recently legalized UWB for commercial use
  Spectrum allocation overlays existing users, but its allowed power level is very low to minimize interference (underlay system)
Data rate scales with the shorter pulse widths made possible with ever faster CMOS circuits
education for life www.rimt.ac.in

## Slide 20: Emerging Systems
Ad hoc wireless networks
Sensor networks
Distributed control networks
education for life www.rimt.ac.in

## Slide 21: Ad-Hoc Networks
Peer-to-peer communications.
No backbone infrastructure.
Routing can be multihop.
Topology is dynamic.
Fully connected with different link SINRs
education for life www.rimt.ac.in
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 22: Design Issues
Ad-hoc networks provide a flexible network infrastructure for many emerging applications.
The capacity of such networks is generally unknown.
Transmission, access, and routing strategies for ad-hoc networks are generally ad-hoc.
Crosslayer design critical and very challenging.
Energy constraints impose interesting design tradeoffs for communication and networking.
education for life www.rimt.ac.in