## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
channel assignment strategies
education for life www.rimt.ac.in

## Slide 3
Cell structure
Implements space division multiplex: base station covers a certain transmission area (cell)
Mobile users communicate only via the base station
Advantages of cell structures:
  higher capacity, higher number of users
  less transmission power needed
  more robust, decentralized
  base station deals with interference locally
Cell sizes from some 100 m in cities to, e.g., 35 km on the country side (GSM) - even more for higher frequencies
education for life www.rimt.ac.in

## Slide 4: Cellular architecture
One low power transmitter per cell
Frequency reuse–limited spectrum
Cell splitting to increase capacity
A
B
Reuse distance: minimum distance between two cells using same channel for satisfactory signal to noise ratio
Measured in # of cells in between
education for life www.rimt.ac.in

## Slide 5: Problems
  Propagation path loss for signal power: quadratic or higher in distance
  fixed network needed for the base stations
  handover (changing from one cell to another) necessary
  interference with other cells:
Co-channel interference:
Transmission on same frequency
Adjacent channel interference:
Transmission on close frequencies
education for life www.rimt.ac.in

## Slide 6: Reuse pattern for reuse distance 2?
One frequency can be (re)used in all cells of the same color
Minimize number of frequencies=colors
education for life www.rimt.ac.in

## Slide 7: Reuse distance 2 – reuse pattern
One frequency can be (re)used in all cells of the same color
education for life www.rimt.ac.in

## Slide 8: Reuse pattern for reuse distance 3?
education for life www.rimt.ac.in

## Slide 9
Reuse distance 3 – reuse pattern
education for life www.rimt.ac.in

## Slide 10
Frequency planning I
Frequency reuse only with a certain distance between the base stations
Standard model using 7 frequencies:
Note pattern for repeating the same color: one north, two east-north
f4
f5
f1
f3
f2
f6
f7
f3
f2
f4
f5
f1
education for life www.rimt.ac.in

## Slide 11: Fixed and Dynamic assignment
Fixed frequency assignment: permanent
  certain frequencies are assigned to a certain cell
  problem: different traffic load in different cells
Dynamic frequency assignment: temporary
  base station chooses frequencies depending on the frequencies already used in neighbor cells
  more capacity in cells with more traffic
  assignment can also be based on interference measurements
education for life www.rimt.ac.in

## Slide 12: 3 cell cluster with 3 sector antennas
f1
f1
f1
f2
f3
f2
f3
f2
f3
h1
h2
h3
g1
g2
g3
h1
h2
h3
g1
g2
g3
g1
g2
g3
education for life www.rimt.ac.in

## Slide 13
Cell breathing
CDM systems: cell size depends on current load
Additional traffic appears as noise to other users
If the noise level is too high users drop out of cells
education for life www.rimt.ac.in

## Slide 14: Hexagon graphs: reuse distance 2
What is the graph for reuse distance 3?
education for life www.rimt.ac.in

## Slide 15: Adjacent channel interference
Receiver filter
f1
f3
f2
interference
Co-site constraint: channels in the same cell must be c0 apart
Adjacent-site constraint: channels assigned to neighboring cells must be c1 apart
Inter-site constraint: channels assigned to cells that are r cells apart must be cr apart
education for life www.rimt.ac.in

## Slide 16: Topics to be covered in next lecture
handoff strategies
education for life www.rimt.ac.in