## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
handoff strategies
education for life www.rimt.ac.in

## Slide 3
Handoff Strategies
When a mobile moves into a different cell while a conversation is in progress, the MSC automatically transfers the call to a new channel belonging to the new base station.
Handoff operation
  identifying a new base station
  re-allocating the voice and control channels with the new base station.
Handoff Threshold
  Minimum usable signal for acceptable voice quality (-90dBm to -100dBm)
  Handoff margin cannot be too large or too small.
  If is too large, unnecessary handoffs burden the MSC
  If is too small, there may be insufficient time to complete handoff before a call is lost.
education for life www.rimt.ac.in

## Slide 4
education for life www.rimt.ac.in

## Slide 5
Handoff must ensure that the drop in the measured signal is not due to momentary fading and that the mobile is actually moving away from the serving base station.
Running average measurement of signal strength should be optimized so that unnecessary handoffs are avoided.
  Depends on the speed at which the vehicle is moving.
  Steep short term average -> the hand off should be made quickly
  The speed can be estimated from the statistics of the received short-term fading signal at the base station
Dwell time: the time over which a call may be maintained within a cell without handoff.
Dwell time depends on
  propagation
  interference
  distance
  speed
education for life www.rimt.ac.in

## Slide 6
Handoff measurement
  In first generation analog cellular systems, signal strength measurements are made by the base station and supervised by the MSC.
  In second generation systems (TDMA), handoff decisions are mobile assisted, called mobile assisted handoff (MAHO)
Intersystem handoff: If a mobile moves from one cellular system to a different cellular system controlled by a different MSC.
Handoff requests is much important than handling a new call.
education for life www.rimt.ac.in

## Slide 7
Practical Handoff Consideration
Different type of users
  High speed users need frequent handoff during a call.
  Low speed users may never need a handoff during a call.
Microcells to provide capacity, the MSC can become burdened if high speed users are constantly being passed between very small cells.
Minimize handoff intervention
  handle the simultaneous traffic of high speed and low speed users.
Large and small cells can be located at a single location (umbrella cell)
  different antenna height
  different power level
Cell dragging problem: pedestrian users provide a very strong signal to the base station
  The user may travel deep within a neighboring cell
education for life www.rimt.ac.in

## Slide 8
education for life www.rimt.ac.in

## Slide 9
Handoff for first generation analog cellular systems
  10 secs handoff time
  is in the order of 6 dB to 12 dB
Handoff for second generation cellular systems, e.g., GSM
  1 to 2 seconds handoff time
  mobile assists handoff
  is in the order of 0 dB to 6 dB
  Handoff decisions based on signal strength, co-channel interference, and adjacent channel interference.
IS-95 CDMA spread spectrum cellular system
  Mobiles share the channel in every cell.
  No physical change of channel during handoff
  MSC decides the base station with the best receiving signal as the service station
education for life www.rimt.ac.in

## Slide 10
Interference and System Capacity
Sources of interference
  another mobile in the same cell
  a call in progress in the neighboring cell
  other base stations operating in the same frequency band
  noncellular system leaks energy into the cellular frequency band
Two major cellular interference
  co-channel interference
  adjacent channel interference
education for life www.rimt.ac.in

## Slide 11
Co-channel Interference and System Capacity
Frequency reuse - there are several cells that use the same set of frequencies
  co-channel cells
  co-channel interference
To reduce co-channel interference, co-channel cell must be separated by a minimum distance.
When the size of the cell is approximately the same
  co-channel interference is independent of the transmitted power
  co-channel interference is a function of
    R: Radius of the cell
    D: distance to the center of the nearest co-channel cell
Increasing the ratio Q=D/R, the interference is reduced.
Q is called the co-channel reuse ratio
education for life www.rimt.ac.in

## Slide 12
For a hexagonal geometry
A small value of Q provides large capacity
A large value of Q improves the transmission quality - smaller level of co-channel interference
A tradeoff must be made between these two objectives
education for life www.rimt.ac.in

## Slide 13
Adjacent Channel Interference
Adjacent channel interference: interference from adjacent in frequency to the desired signal.
  Imperfect receiver filters allow nearby frequencies to leak into the passband
  Performance degrade seriously due to near-far effect.
education for life www.rimt.ac.in

## Slide 14
Adjacent channel interference can be minimized through careful filtering and channel assignment.
Keep the frequency separation between each channel in a given cell as large as possible
A channel separation greater than six is needed to bring the adjacent channel interference to an acceptable level.
education for life www.rimt.ac.in

## Slide 15: Topics to be covered in next lecture
interference and system capacity
education for life www.rimt.ac.in