## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
Interference and system capacity
education for life www.rimt.ac.in

## Slide 3
Interference and System Capacity
Sources of interference
  another mobile in the same cell
  a call in progress in the neighboring cell
  other base stations operating in the same frequency band
  noncellular system leaks energy into the cellular frequency band
Two major cellular interference
  co-channel interference
  adjacent channel interference
education for life www.rimt.ac.in

## Slide 4
Co-channel Interference and System Capacity
Frequency reuse - there are several cells that use the same set of frequencies
  co-channel cells
  co-channel interference
To reduce co-channel interference, co-channel cell must be separated by a minimum distance.
When the size of the cell is approximately the same
  co-channel interference is independent of the transmitted power
  co-channel interference is a function of
    R: Radius of the cell
    D: distance to the center of the nearest co-channel cell
Increasing the ratio Q=D/R, the interference is reduced.
Q is called the co-channel reuse ratio
education for life www.rimt.ac.in

## Slide 5
For a hexagonal geometry
A small value of Q provides large capacity
A large value of Q improves the transmission quality - smaller level of co-channel interference
A tradeoff must be made between these two objectives
education for life www.rimt.ac.in

## Slide 6
Cell Splitting
Split congested cell into smaller cells.
  Preserve frequency reuse plan.
  Reduce transmission power.
microcell
Reduce R to R/2

## Slide 7
Illustration of cell splitting within a 3 km by 3 km square

## Slide 8
Sectoring
Decrease the co-channel interference and keep the cell radius R unchanged
  Replacing single omni-directional antenna by several directional antennas
  Radiating within a specified sector
education for life www.rimt.ac.in

## Slide 9
Interference Reduction
position of the mobile
interference cells
education for life www.rimt.ac.in

## Slide 10
Microcell Zone Concept
Antennas are placed at the outer edges of the cell
Any channel may be assigned to any zone by the base station
Mobile is served by the zone with the strongest signal.
Handoff within a cell
  No channel re-assignment
  Switch the channel to a different zone site
Reduce interference
  Low power transmitters are employed
education for life www.rimt.ac.in

## Slide 11: Topics to be covered in next lecture
improving coverage and capacity in cellular systems
education for life www.rimt.ac.in