## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
Authentication header (AH)
education for life www.rimt.ac.in

## Slide 3: Authentication Header
AH Header Format
AH Parameters
Packet Processing
education for life www.rimt.ac.in

## Slide 4: AH Header Format
Next Header
Payload Len
RESERVED
Security Parameters Index (SPI)
Sequence Number Field
Authentication Data (Variable)
education for life www.rimt.ac.in

## Slide 5: AH Parameters
Next Header - Next header ID
Payload Length – Number of 32-bit words in the AH header minus 2 (IPv6 minus 1 64-bit word)
SPI – 32-bit value that together with the destination IP address uniquely identifies the Security Association for this datagram
education for life www.rimt.ac.in

## Slide 6: Sequence Number Generation
Sender's counter is initialized to 0 when the SA is established.
Sender increments the counter by 1
  New SA is negotiated upon rollover for both sender and receiver
32-bits
Sender must include
Receiver may or maynot use it
education for life www.rimt.ac.in

## Slide 7: Authentication Data
Authentication Data field is a variable length field that contains the Integrity Check Value (ICV) for this packet
Multiple of 32-bits
The ICV algorithm is specified in the SA
  Usually an HMAC (keyed hash)
  ICV is calculated over the Immutable and Predictable values in the IP header, AH header, padding, upper level protocols and payload, etc.
education for life www.rimt.ac.in

## Slide 8: Authenticated Data
Immutable
    Version, Payload Length, Next Header, Source Address, Destination Address without Routing Extension Header
Mutable but predictable
    Destination Address with Routing Extension Header
Mutable ( zeroed prior to ICV cal)
    Class, Flow Label, Hop Limit
education for life www.rimt.ac.in

## Slide 9: Authenticated Data (cont'd)
Extension Headers containing Options ( Hop-by-Hop and Dest Headers
    Bit-3 of the Type indicates whether it can change in route
      Changeable – zeroed for ICV cal
      Unchangeable – include in the ICV cal
    Padding
Fragmentation
    If required happens after the AH Header
    May happen after AH Header is applied, then reassembly must happen and the the AH Header is processed
education for life www.rimt.ac.in

## Slide 10: Authenticated Data (cont'd)
The AH extension header
  Especially important is the Sequence Number for anti-replay
Subsequent extension headers
The payload
Usually HMAC-SHA-n
education for life www.rimt.ac.in

## Slide 11: AH Location in the list of Headers
IPv6 considerations only
  At the end of all extension headers except possibly Destination Headers
IPv6
Header
AH
Payload
Older Ipv6
Header
AH
Payload
New IPv6
Header
Ext Headers
Transport Mode
Tunnel Mode
education for life www.rimt.ac.in

## Slide 12: Outbound Packet Processing
Match packet's selectors against the outbound policies in the SPD
SA Lookup
Sequence Number Generation
ICV Calculation
Fragmentation of the IPSec datagram if necessary
education for life www.rimt.ac.in

## Slide 13: Inbound Packet Processing
Datagram Reassembly
SA Lookup
    Based on IP address
    Security Protocol
    The SPI
ICV Verification
    Calc'ed over Immutable fields
    Mutable but predictable fields
    Options and Payload
Sequence Number Verification
education for life www.rimt.ac.in

## Slide 14: Topics to be covered in next lecture
Encapsulating Security Payload (ESP).
education for life www.rimt.ac.in