## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
Adhoc versus Cellular networks
education for life www.rimt.ac.in

## Slide 3: Comparisons between Cellular and Ad Hoc Wireless Networks (I)
Cellular Networks | Ad Hoc Wireless Networks
Fixed infrastructure-based | Infrastructureless
Guaranteed bandwidth (designed for voice traffic) | Shared radio channel (more suitable for best-effort data traffic)
Centralized routing | Distributed routing
Circuit-switched (evolving toward packet switching) | Packet-switched (evolving toward emulation of circuit switching)
Seamless connectivity (low call drops during handoffs) | Frequent path breaks due to mobility
High cost and time of deployment | Quick and cost-effective deployment
Reuse of frequency spectrum through geographical channel reuse | Dynamic frequency reuse based on carrier sense mechanism
Easier to employ bandwidth reservation | Bandwidth reservation requires complex medium access control protocols
education for life www.rimt.ac.in

## Slide 4: Comparisons between Cellular and Ad Hoc Wireless Networks (II)
Cellular Networks | Ad Hoc Wireless Networks
Application domains include mainly civilian and commercial sectors | Application domains include battlefields, emergency search and rescue operations, and collaborative computing
High cost of network maintenance (backup power source, staffing, etc.) | Self-organization and maintenance properties are built into the network
Mobile hosts are of relatively low complexity | Mobile hosts require more intelligence (should have a transceiver as well as routing/switching capability)
Major goals of routing and call admission are to maximize the call acceptance ratio and minimize the call drop ratio | Main aim of routing is to find paths with minimum overhead and also quick reconfiguration of broken paths
Widely deployed and currently in the third generation of evolution | Several issues are to be addressed for successful commercial deployment even though widespread use exists in defense
education for life www.rimt.ac.in

## Slide 5: Issues in Ad hoc Wireless Networks
Medium access scheme
  Distributed operation is required.
  Synchronization is required in TDMA-based systems.
  Hidden terminals are nodes hidden from a sender.
  Exposed terminals are exposed nodes preventing a sender from sending.
  Throughput needs to be maximized.
  Access delay should be minimized.
  Fairness refers to provide an equal share to all competing nodes.
  Real-time traffic support is required for voice, video, and real-time data.
  Resource reservation is required for QoS.
  Ability to measure resource availability handles the resources.
  Capability for power control reduces the energy consumption.
  Adaptive rate control refers to the variation in the data bit rate.
  Use of directional antennas has advantages including increased spectrum reuse, reduced interference, and reduced power consumption.
education for life www.rimt.ac.in

## Slide 6: Issues in Ad hoc Wireless Networks
Routing
  Mobility
  Bandwidth constraint
  Error-prone and shared channel: wireless channel (10-5 to 10-3), wired channel (10-12 to 10-9)
  Location-dependent contention depends on the number of nodes.
  Other resource constraints such as computing power, battery power
  Minimum route acquisition delay
  Quick route reconfiguration
  Loop-free routing
  Distributed routing approach
  Minimum control overhead
  Scalability
  Provisioning of QoS
  Support for time-sensitive traffic: hard real-time and soft real-time traffic
  Security and privacy
education for life www.rimt.ac.in

## Slide 7: Issues in Ad hoc Wireless Networks
Provisioning of multiple links among the nodes in an ad hoc network results in a mesh-shaped structure. The mesh-shaped multicast routing structure work well in a high-mobility environment.
The issues in multicast routing protocols are:
  Robustness: It must be able to recover and reconfigure quickly.
  Efficiency: It should make a minimum number of transmissions to deliver a packet.
  Control overhead: It demands minimal control overhead.
  Quality of service: QoS support is essential.
  Efficient group management needs to be performed with minimal exchange of control messages.
  Scalability: It should be able to scale for a large network.
  Security is important.
education for life www.rimt.ac.in

## Slide 8: Issues in Ad hoc Wireless Networks
The objectives of the transport layer protocols include:
  Setting up and maintaining end-to-end connections
  Reliable end-to-end delivery of data packets
  Flow control
  Congestion control
Connectionless transport layer protocol (UDP), unaware of high contention, increases the load in the network.
Pricing Schemes need to incorporate service compensation.
Quality of Service Provisioning
  QoS parameters based on different applications
  QoS-aware routing uses QoS parameters to find a path.
  QoS framework is a complete system that aims at providing the promised services to each users.
education for life www.rimt.ac.in

## Slide 9: Issues in Ad hoc Wireless Networks
Self-Organization is required in ad hoc wireless networks:
  Neighbor discovery
  Topology organization
  Topology reorganization
Security
  Denial of service
  Resource consumption
    Energy depletion: deplete the battery power of critical nodes
    Buffer overflow: flooding the routing table or consuming the data packet buffer space
  Host impersonation: A compromised node can act as another node.
  Information disclosure: a compromised node can act as an informer.
  Interference: jam wireless communication by creating a wide-spectrum noise.
education for life www.rimt.ac.in

## Slide 10: Issues in Ad hoc Wireless Networks
Addressing and Service Discovery is essential because of absence of a centralized coordinator.
Energy Management
  Transmission power management: The radio frequency (RF) hardware design should ensure minimum power consumption.
  Battery energy management is aimed at extending the battery life.
  Processor power management: The CPU can be put into different power saving modes.
  Devices power management: Intelligent device management can reduce power consumption of a mobile node.
Scalability is expected in ad hoc wireless networks.
education for life www.rimt.ac.in

## Slide 11: Issues in Ad hoc Wireless Networks
Deployment considerations
  Low cost of deployment
  Incremental deployment
  Short deployment time
  Reconfigurability
  Scenario of deployment
    Military deployment
    Emergency operations deployment
    Commercial wide-area deployment
    Home network deployment
  Required longevity of network
  Area of coverage
  Service availability
  Operational integration with other infrastructure
  Choice of protocols at different layers should be taken into consideration.
education for life www.rimt.ac.in
education for life www.rimt.ac.in

## Slide 12: Issues of Ad hoc Wireless Internet
Gateways
  Gateway nodes are the entry points to the wired Internet and generally owned and operated by a service provider.
  Perform the following tasks: keeping track of the end users, band-width fairness, address, and location discovery.
Address mobility
  Solutions such as Mobile IP can be used.
Routing
  Specific routing protocols for ad hoc networks are required.
Transport layer protocol
  Split approaches that use traditional wired TCP for the wired part and a specialized transport layer protocol for the ad hoc wireless network part.
Load balancing
  Load balancing techniques are essential to distribute the load so as to avoid the situation where the gateway nodes become bottleneck nodes.
education for life www.rimt.ac.in

## Slide 13: Issues of Ad hoc Wireless Internet
Pricing/billing
  It is important to introduce pricing/billing strategies for the ad hoc wireless internet.
Provisioning of security
  It is essential to include security mechanisms in the ad hoc wireless Internet.
QoS support
  Voice over IP (VoIP) and multimedia applications require the QoS support.
Service, address, and location discovery
  Service discovery refers to the activity of discovering or identifying the party which provides a particular service or resource.
  Address discovery refers to the services such as address resolution protocol (ARP) or domain name service (DNS).
  Location discovery refers to different activities such as detecting the location of a particular mobile node.
education for life www.rimt.ac.in

## Slide 14: Topics to be covered in next lecture
Ad hoc Network architecture
education for life www.rimt.ac.in