## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
Ad hoc Network architecture
education for life www.rimt.ac.in

## Slide 3: Advent of Ad hoc Wireless Networks
The principle behind ad hoc networking is multi-hop relaying in which messages are sent from the source to the destination by relaying through the intermediate hops (nodes).
In multi-hop wireless networks, communication between two end nodes is carried out through a number of intermediate nodes whose function is to relay information from one point to another. A static string topology is an example of such network:
In the last few years, efforts have been focused on multi-hop "ad hoc" networks, in which relaying nodes are in general mobile, and communication needs are primarily between nodes within the same network.
education for life www.rimt.ac.in

## Slide 4: Advent of Ad hoc Wireless Networks
An examples of such developments is the Bluetooth standard that is one of the first commercial realizations of ad hoc wireless networking developed by Bluetooth Special Interest Group (SIG):
  A piconet formed by a group of nodes establishes a single-hop (master node) point-to-point wireless link.
  A scatternet formed by multiple piconets (master nodes) can establish a multi-hop wireless network.
Though the IEEE 802.11 protocols have developed for the wireless networks, they don’t function well in multi-hop networks.
Realizing the necessity of open standards in this emerging area of computer communication, the mobile ad hoc networks (MANET) standards are being developed by the Internet Working Tasking Force (IETF) MANET working group.
education for life www.rimt.ac.in

## Slide 5: Advent of Ad hoc Wireless Networks
Even though ad hoc wireless networks are expected to work in the absence of any fixed infrastructure, recent advances in wireless network architectures enable the mobile ad hoc nodes to function in the presence of infrastructure
Multi-hop cellular networks (MCNs), self-organizing packet radio ad hoc networks with overlay (SOPRANO), and mesh networks are examples of such types of networks.
Mesh networks serve as access networks that employ multi-hop wireless forwarding by non-mobile nodes to relay traffic to and from the wired Internet. In such an environment, hybrid technologies and/or hierarchical network organization can be used for ad hoc and infrastructure wireless links.
education for life www.rimt.ac.in

## Slide 6: Cellular and Ad Hoc Wireless Networks
The following figure represents different wireless networks.
  Infrastructure: cellular wireless networks
  Ad hoc: wireless sensor networks
  Hybrid: mesh networks
Cellular Wireless
Networks
Hybrid Wireless Networks
Wireless Mesh
Networks
Wireless Sensor
Networks
education for life www.rimt.ac.in

## Slide 7: Applications of Ad hoc Wireless Networks
Military applications
  Ad hoc wireless networks is useful in establishing communication in a battle field.
Collaborative and Distributed Computing
  A group of people in a conference can share data in ad hoc networks.
  Streaming of multimedia objects among the participating nodes.
Emergency Operations
  Ad hoc wireless networks are useful in emergency operations such as search and rescue, and crowd control.
A Wireless Mesh Network is a mesh network that is built upon wireless communications and allows for continuous connections and reconfiguration around blocked paths by "hopping" from node to node until a connection can be established.
education for life www.rimt.ac.in

## Slide 8: Wireless Mesh Networks
In a wireless mesh network, multiple nodes cooperate to relay a message to its destination. The mesh topology enhances the overall reliability of the network, which is particularly important when operating in harsh industrial environments.
education for life www.rimt.ac.in

## Slide 9: Wireless Mesh Networks
The investment required in wireless mesh networks is much less than in the cellular network counterparts.
Such networks are formed by placing wireless replaying equipment spread across the area to be covered by the network.
The possible deployment scenarios include:
  Residential zones (where broadband Internet connectivity is required)
  Highways (where a communication facility for moving automobiles is required)
  Business zones (where an alternate communication system to cellular networks is required)
  Important civilian regions (where a high degree of service availability is required)
  University campuses (where inexpensive campus-wide network coverage can be provided)
education for life www.rimt.ac.in

## Slide 10: Wireless Mesh Networks
Wireless mesh networks should be capable of self-organization and maintenance.
Advantages
  High data rate
  Quick and low cost of deployment
  Enhanced services
  High scalability
  Easy extendability
  High availability
  Low cost per bit
  High availability
  Low cost per bit
It operates at 2.4 GHz or 5 GHz
Data rates of 2 Mbps to 60 Mbps can be supported.
education for life www.rimt.ac.in

## Slide 11: Wireless Sensor Networks
Wireless Sensor Networks are a special category of ad hoc networks that are used to provide a wireless communication infrastructure among the sensors deployed in a specific application domain.
A sensor network is a collection of a large number of sensor nodes that are deployed in a particular region.
Distinct properties of wireless sensor networks:
  Mobility of nodes are not needed in all cases in wireless sensor networks.
  The size of the network is much larger than that in a typical ad hoc wireless network.
  The density of nodes in a sensor network varies with the domain of application.
  The power constraints in sensor networks are much more stringent than those in ad hoc wireless networks.
education for life www.rimt.ac.in

## Slide 12: Wireless Sensor Networks
Distinct properties of wireless sensor networks:
  The power source can be classified into three categories:
    Replenishable power resource
    Non- Replenishable power source
    Regenerative power source
  Data/information fusion aims at processing the sensed data at the intermediate nodes and relaying the outcome to the monitor node.
  The communication traffic pattern varies with the domain of applications.
education for life www.rimt.ac.in

## Slide 13: Hybrid Wireless Networks
Hybrid Wireless Networks
  Multi-hop cellular networks (MCNs) allows the transmission through the base stations or multi-hop of mobile nodes.
  Integrated cellular ad hoc relay (iCAR) is a system that combines conventional cellular technology with Ad hoc Relay Station (ARS) technology. In this system cellular stations will relay or reroute calls from the congested cell to an adjacent one that is not congested.
Advantages
  Higher capacity than cellular networks
  Increased flexibility and reliability in routing
  Better coverage and connectivity
education for life www.rimt.ac.in

## Slide 14: Issues in Ad hoc Wireless Networks
Medium access scheme
  Distributed operation is required.
  Synchronization is required in TDMA-based systems.
  Hidden terminals are nodes hidden from a sender.
  Exposed terminals are exposed nodes preventing a sender from sending.
  Throughput needs to be maximized.
  Access delay should be minimized.
  Fairness refers to provide an equal share to all competing nodes.
  Real-time traffic support is required for voice, video, and real-time data.
  Resource reservation is required for QoS.
  Ability to measure resource availability handles the resources.
  Capability for power control reduces the energy consumption.
  Adaptive rate control refers to the variation in the data bit rate.
  Use of directional antennas has advantages including increased spectrum reuse, reduced interference, and reduced power consumption.
education for life www.rimt.ac.in

## Slide 15: Issues in Ad hoc Wireless Networks
Routing
  Mobility
  Bandwidth constraint
  Error-prone and shared channel: wireless channel (10-5 to 10-3), wired channel (10-12 to 10-9)
  Location-dependent contention depends on the number of nodes.
  Other resource constraints such as computing power, battery power
  Minimum route acquisition delay
  Quick route reconfiguration
  Loop-free routing
  Distributed routing approach
  Minimum control overhead
  Scalability
  Provisioning of QoS
  Support for time-sensitive traffic: hard real-time and soft real-time traffic
  Security and privacy
education for life www.rimt.ac.in

## Slide 16: Issues in Ad hoc Wireless Networks
Provisioning of multiple links among the nodes in an ad hoc network results in a mesh-shaped structure. The mesh-shaped multicast routing structure work well in a high-mobility environment.
The issues in multicast routing protocols are:
  Robustness: It must be able to recover and reconfigure quickly.
  Efficiency: It should make a minimum number of transmissions to deliver a packet.
  Control overhead: It demands minimal control overhead.
  Quality of service: QoS support is essential.
  Efficient group management needs to be performed with minimal exchange of control messages.
  Scalability: It should be able to scale for a large network.
  Security is important.
education for life www.rimt.ac.in

## Slide 17: Issues in Ad hoc Wireless Networks
The objectives of the transport layer protocols include:
  Setting up and maintaining end-to-end connections
  Reliable end-to-end delivery of data packets
  Flow control
  Congestion control
Connectionless transport layer protocol (UDP), unaware of high contention, increases the load in the network.
Pricing Schemes need to incorporate service compensation.
Quality of Service Provisioning
  QoS parameters based on different applications
  QoS-aware routing uses QoS parameters to find a path.
  QoS framework is a complete system that aims at providing the promised services to each users.
education for life www.rimt.ac.in

## Slide 18: Issues in Ad hoc Wireless Networks
Self-Organization is required in ad hoc wireless networks:
  Neighbor discovery
  Topology organization
  Topology reorganization
Security
  Denial of service
  Resource consumption
    Energy depletion: deplete the battery power of critical nodes
    Buffer overflow: flooding the routing table or consuming the data packet buffer space
  Host impersonation: A compromised node can act as another node.
  Information disclosure: a compromised node can act as an informer.
  Interference: jam wireless communication by creating a wide-spectrum noise.
education for life www.rimt.ac.in

## Slide 19: Topics to be covered in next lecture
Protocols
MAC protocols
education for life www.rimt.ac.in