## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
Routing protocols

## Slide 3: Routing
Recall: There are two parts to routing IP packets:
1. How to pass a packet from an input interface to the output interface of a router (packet forwarding) ?
2. How to find and setup a route ?
We already discussed the packet forwarding part
There are two approaches for calculating the routing tables:
  Static Routing
  Dynamic Routing: Routes are calculated by a routing protocol
education for life www.rimt.ac.in

## Slide 4: IP Routing
education for life www.rimt.ac.in

## Slide 5: Components of a Routing Algorithm
A procedure for sending and receiving reachability information about network to other routers
A procedure for calculating optimal routes
  Routes are calculated using a shortest path algorithm:
    Goal: Given a network were each link is assigned a cost. Find the path with the least cost between two networks with minimum cost.
A procedures for reacting to and advertising topology changes
education for life www.rimt.ac.in

## Slide 6: Approaches to Shortest Path Routing
There are two basic routing algorithms found on the Internet.
1. Distance Vector Routing
Each node knows the distance (=cost) to its directly connected neighbors
A node sends periodically a list of routing updates to its neighbors.
If all nodes update their distances, the routing tables eventually converge
New nodes advertise themselves to their neighbors
2. Link State Routing
Each node knows the distance to its neighbors
The distance information (=link state) is broadcast to all nodes in the network
Each node calculates the routing tables independently
education for life www.rimt.ac.in

## Slide 7: Routing Algorithms in the Internet
Distance Vector
Routing Information Protocol (RIP)
Gateway-to-Gateway Protocol (GGP)
Exterior Gateway Protocol (EGP)
Interior Gateway Routing Protocol (IGRP)
Link State
Intermediate System - Intermediate System (IS-IS)
Open Shortest Path First (OSPF)
education for life www.rimt.ac.in

## Slide 8: A network as a graph
In the following, networks are represented as a network graph:
  nodes are connected by networks
      network can be a link or a LAN
  network interface has cost
  networks are destinations
  Net(v,w) is an IP address of a network
For ease of notation, we often replace the clouds between nodes by simple links.
education for life www.rimt.ac.in

## Slide 9: Distance Vector Algorithm: Routing Table
Net(v,w): Network address of the network between v and w The network can be a link, but could also be a LAN
c(v,w): cost to transmit on the interface to network Net(v,w)
education for life www.rimt.ac.in

## Slide 10: Distance Vector Algorithm: Messages
Nodes send messages to their neighbors which contain routing table entries
A message has the format: [Net , D(v,Net)] means“My cost to go to Net is D (v,Net)”
v
n
[Net , D(v,Net)]
education for life www.rimt.ac.in

## Slide 11: Distance Vector Algorithm: Sending Updates
Periodically, each node v sends the content of its routing table to its neighbors:
education for life www.rimt.ac.in

## Slide 12: Initiating Routing Table I
Suppose a new node v becomes active.
The cost to access directly connected networks is zero:
      D (v, Net(v,m)) = 0
      D (v, Net(v,w)) = 0
      D (v, Net(v,n)) = 0
education for life www.rimt.ac.in

## Slide 13: Initiating Routing Table II
New node v sends the routing table entry to all its neighbors:
education for life www.rimt.ac.in

## Slide 14: Initiating Routing Table III
Node v receives the routing tables from other nodes and builds up its routing table
education for life www.rimt.ac.in

## Slide 15: Updating Routing Tables I
Suppose node v receives a message from node m: [Net,D(m,Net)]
if ( D(m,Net) + c (v,m) < D (v,Net) ) {
  Dnew (v,Net) := D (m,Net) + c (v,m); Update routing table;
  send message [Net, Dnew (v,Net)] to all neighbors
}
Node v updates its routing table and sends out further messages if the message reduces the cost of a route:
education for life www.rimt.ac.in

## Slide 16: Updating Routing Tables II
Before receiving the message:
Suppose D (m,Net) + c (v,m) < D (v,Net):
education for life www.rimt.ac.in

## Slide 17: Characteristics of Distance Vector Routing
Periodic Updates: Updates to the routing tables are sent at the end of a certain time period. A typical value is 90 seconds.
Triggered Updates: If a metric changes on a link, a router immediately sends out an update without waiting for the end of the update period.
Full Routing Table Update: Most distance vector routing protocol send their neighbors the entire routing table (not only entries which change).
Route invalidation timers: Routing table entries are invalid if they are not refreshed. A typical value is to invalidate an entry if no update is received after 3-6 update periods.
education for life www.rimt.ac.in

## Slide 18: RIP - Routing Information Protocol
A simple intradomain protocol
Straightforward implementation of Distance Vector Routing
Each router advertises its distance vector every 30 seconds (or whenever its routing table changes) to all of its neighbors
RIP always uses 1 as link metric
Maximum hop count is 15, with “16” equal to “”
Routes are timeout (set to 16) after 3 minutes if they are not updated
education for life www.rimt.ac.in

## Slide 19: RIPv1 Packet Format
One RIP message can have up to 25 route entries
1: request 2: response
2: for IP
0…0: request full rou-ting table
Address of destination
Cost (measured in hops)
1: RIPv1
education for life www.rimt.ac.in

## Slide 20: RIPv2 Packet Format
One RIP message can have up to 25 route entries
1: request 2: response
2: for IP
0…0: request full rou-ting table
Address of destination
Cost (measured in hops)
2: RIPv2
education for life www.rimt.ac.in

## Slide 21: RIP Messages
This is the operation of RIP in routed. Dedicated port for RIP is UDP port 520.
Two types of messages:
  Request messages
    used to ask neighboring nodes for an update
  Response messages
    contains an update
education for life www.rimt.ac.in

## Slide 22: Topics to be covered in next lecture
Ad hoc Technologies
education for life www.rimt.ac.in