## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
Wireless Communication System
2G Cellular networks
education for life www.rimt.ac.in

## Slide 3
First Generation Cellular Systems
  First generation (1G) of cellular systems introduced in the late 1970s and early 1980s
  Evolved out of the growing number of mobile communication users
  The use of semiconductor technology and microprocessors made mobile devices smaller and lighter
  1G systems were based on analogue communication in the 900MHz frequency range
  Voice transmission only – easy to tap
  The most prominent 1G systems are
    Advanced Mobile Phone Systems (AMPS) - America
    Nordic Mobile Telephone (NMT) - France
    Total Access Communications System (TACS) – UK
      Jan 1985 Vodafone introduced the TACS system
education for life www.rimt.ac.in

## Slide 4
First Generation Cellular Systems
Frequency Division Multiple Access (FDMA)
  Splits allocated spectrum into 30 channels, each channel is 30kHz
  Allocates a single channel to each established phone call
  The channel is agreed with the serving base-station before transmission takes place on agreed and reserved channel
  Channel used by device to transmit and receive on this channel
  Ineffective methods since each analogue channel can only be used by one user at a time
  FDMA does not take full advantage of available spectrum
education for life www.rimt.ac.in

## Slide 5
Frequency Division Multiple Access (FDMA)
First Generation Cellular Systems
Frequency
education for life www.rimt.ac.in

## Slide 6
Second Generation Cellular Systems
  Development driven by the need to improve speech quality, system capacity, coverage and security
  First system that used digital transmission
  Examples of Second Generation (2G) cellular systems ...
    Digital AMPS (D-AMPS) in the US,
    Personal Digital Communication (PDC) in Japan,
    Intrim Standard `94 (IS-94) in Korea and the US
    Global System for Mobile Communication (GSM)
  The GSM standard was defined by ETSI in 1989
    Originally called „Groupe Spéciale Mobile“ which later changed to the English version
  A majority of countries over the world have adopted GSM900 and the GSM1800 which are all based on the same original GSM specification.
    The US uses an additional GSM 1900
education for life www.rimt.ac.in

## Slide 7
GSM System – Radio Interface
  Base frequency: 900MHz
  Two frequency bands of 25MHz each
  (890-915MHz uplink, 935-960MHz downlink)
  Channel spacing 200kHz
  124 channels per frequency band
  Gaussian Minimum Shift Keyring (GMSK)
  Time Division Multiple Access (TDMA)
  Hard Handover (MAHO)
  Maximum Bandwidth available: 9600 bits per second
    Full Rate = 9600bps, Half rate 4800 Bps
education for life www.rimt.ac.in

## Slide 8
GSM System – Modulation
  Gaussian Minimum Shift Keying (GMSK) – Phase modulation technique
  Intended to encode the binary with the minimum of changes to the carrier wave.
  The carrier wave only changes when a sequence of data is broken
  The phase of the signal varies linearly with exactly ±90deg
  Technique gives fairly good spectral efficiency and constant signal amplitude
education for life www.rimt.ac.in

## Slide 9
GSM System – Multiple Access
Time Division Multiple Access (TDMA)
  Allows larger transmission rates than in an FDMA system
  Used in combination with FDMA
  Based on the idea to break individual frequencies into 8 timeslots of is 0.577 ms length (total 4.615ms) – these are referred to as a frame
  Each mobile device uses a particular slot different from slots used by other users
  Information transmitted in one slot is referred to as burst
  To allow transmission all voice communication needs to be converted into binary
  TDMA requires timeslot synchronisation
education for life www.rimt.ac.in

## Slide 10
Time Division Multiple Access (TDMA)
  Guard Time: Interval between bursts used to avoid overlapping
  Preamble: First part of the burst
  Message: Part of burst that includes user data
  Postamble: Last part of burst – used to initialise following burst
Slot 1
Slot 2
Slot 8
Slot 8
Slot 1
Frame 1
Frame N
Multiframe
Guard Time
Preamble
Message
Postamble
Guard Time
Slot
Slot i
……..
GSM System – Multiple Access
education for life www.rimt.ac.in

## Slide 11
Time Division Multiple Access (TDMA)
GSM System – Multiple Access
Frequency
Time
education for life www.rimt.ac.in

## Slide 12
Code Division Multiple Access (CDMA)
  Multiple access technique used by american System (NOT used by the European GSM system)
  Based on the spread-spectrum technique:
    „Spread spectrum“ indicates that the signal occupies more spectrum than in FDMA and TDMA system
    Transmission mode where the transmitted data occupies a larger bandwidth than that required to transfer data
  Access technique realised before transmission by addition of a code that is independent of the data sequence
    code used at the receive end which must operate synchronized with the transmitter, to despread the received signal in order to recover the initial data
  Allows many devices to transmit simultaneously in the same frequency band
GSM System – Multiple Access
education for life www.rimt.ac.in

## Slide 13
Code Division Multiple Access (CDMA)
Code
Frequency
Time
Channel 1
Channel 2
Channel 3
Channel N
GSM System – Multiple Access
education for life www.rimt.ac.in

## Slide 14
Code Division Multiple Access (CDMA)
  Principle: Each MH is allocated a random sequence or code – this must be different and orthogonal or quasi-orthogonal (i.e. decorrelated) from all other sequences
  CDMA provides protection against multipath fading interference, privacy, interference rejection, anti-jamming capability, low probability of interception and allows macrodiversity
  Three basic spread-spectrum techniques are defined:
    Direct Sequence CDMA – DS-CDMA
    Fast Frequency Hopping CDMA – FH-CDMA
    Time Hopping CDMA – TH-CDMA
GSM System – Multiple Access
education for life www.rimt.ac.in

## Slide 15
GSM System – Handover
Hard Handover Scheme
  Mobile-assisted handover (MAHO) as mobile measure signal strength but network-controlled as the network makes decision
  The mobile device changes over to the new base-stations with a short interruption of the connection
  To make sure the interruption is as short as possible the path to the new base-station is established in advance through the network before changing over
  Switching to the new path and rerouting of the transmitted information are performed simultaneously
  Advantage: The hard handover only uses one channel at any time
  Disadvantage: Possible loss of connection – dropped call
education for life www.rimt.ac.in

## Slide 16
Hard Handover
GSM System – Handover
education for life www.rimt.ac.in

## Slide 17
GSM System – Subscriber Identification
SIM Essential component for the GSM Network
  GSM system introduced Subscriber Identity Card (SIM)
  SIM card is a chip based smart card that stores ...
    Identity of subscriber
    Personal password
    Subscription data
    Temporary Number
    Authentication and ciphering algorithms, etc.
  Use of SIM cards allows the user to personalise mobile device (e.g. Access to services, routing of calls)
  Required to be able to access GSM system
  User will only have access to GSM services with mobile device if he/she has already subscribed to these services
  User may have to enter a Personal Identification Number (PIN)
education for life www.rimt.ac.in

## Slide 18
GSM System – Location Management
  GSM consists of three major systems:
    The Switching System (SS)
    Base-station System (BSS)
    Operation and Support System (OSS)
  The Switching System performs call processing and subscriber related functions
  The system contains the following functional units
    Home Location Register (HLR)
    Mobile Switching Center (MSC)
    Visitor Location Register (VLR)
    Authentication Center (AUC)
    Equipment Identity Register (EIR)
education for life www.rimt.ac.in

## Slide 19
  HLR is the most important database
    Storage and management of subscriptions
    Permanent data includes:
      Subscribers‘s service profile
      Subscribers‘s location information
      Subscriber‘s activity status
    Subscribing to a particular provider‘s service registers you in the HLR of that provider
  The MSC performs the telephony switching functions of the network
    Controlls call to and from other telephone and data systems
    Also performs functions such as
      Toll ticketing
      Network interfacing
      Common Channel signalling
GSM System – Location Management
education for life www.rimt.ac.in

## Slide 20
  VLR contains data on visiting (roaming) subscribers
    Integrated with the MSC
    When a roamer enters the service area the VLR queries the appropriate HLR
    If a roamer makes a call the VLR will already have the information it needs for call setup
  The AUC verifies the identity of the user and ensures and ensures the confidentiality of each call
    By provide authenticity and encryption parameters for every call
    Protects network operators from fraud
    Assures a certain level of security for the content of each call
  The EIR is a database that includes info solely about the identity mobile equipment
    Prevents calls from stolen, unauthorised or defective mobile devices
GSM System – Location Management
education for life www.rimt.ac.in

## Slide 21
GSM System – Location Management
VLR
MSC
VLR
MSC
HLR
MSC Mobile Switching Center
VLR Visitor Location Register
HLR Home Location Register
education for life www.rimt.ac.in

## Slide 22
GSM System – Services
Services provided by GSM system:
  Teleservices
    Services that relate to the terminal equipment (e.g. Telephone, videotext and mail)
  Data Services
    Different services available, dependin on end-to-end transmission type, transmission mode, terminal capability
    Supports data rates of 300bps up to 9600bps
  Facsimile
    Group III Standard
  Short Message Service
    Point-to-point transmission of alphanumeric messages with a maximum of 160 characters
    Messages saved on SIM
education for life www.rimt.ac.in

## Slide 23
GSM System – Services
SMS:
  Allows a text message to be sent using 7-bit alaphnumeric characters based on the western alaphbet
  ETSI standard for SMS is detailed in “GSM 03.40”
    Two character Sets
      ASCII + limited additional European characters (GSM Default)
      Unicode
  The success was never planned for!
    It was designed as a replacement for the pager, which is one way text communication
education for life www.rimt.ac.in

## Slide 24: GSM System – Services
SMS Continued
  Transfers the SMS message in a single packet
    Octet = 8 Bytes
SCA | Service Centre Address | MR | Message Reference | PID | Protocol Identifier
PDU Type | Protocol Data Unit Type | DA | Destination Address | DCS | Data Coding Scheme
VP | Validity Period | UDL | User Data Length | UD | User Data
education for life www.rimt.ac.in

## Slide 25: GSM System – Services
SMS Continued
  Infrastructure
SMSC = Short Message Service Centre
HLR = Home Location Register
SMSC
GSM SMS Infrastructure
Base
Station
Base
Station
HLR
education for life www.rimt.ac.in

## Slide 26: Topics to be covered in next lecture
Evolution for 2.5G TDMA Standards
education for life www.rimt.ac.in