## Slide 1: COMPUTER NETWORKS-II / BTCS-3501
Department of Computer Science & Engineering
Prepared by: Er. Jasdeep Singh
Course Name: B.Tech CSE Semester: 5th
education for life www.rimt.ac.in

## Slide 2: Topics to be covered
Introduction to 3G networks
education for life www.rimt.ac.in

## Slide 3: Route to 3G
1G: analog
2G : 1st digital mobile telephony
2.5G: transition from 2G to 3G
3G standard: IMT 2000
education for life www.rimt.ac.in

## Slide 4: 3G- Advantages
3G phones promise :-
Improved digital voice communications
Larger Bandwidth – Higher Data rate
Greater subscriber capacity
Fast packet-based data services like e-mail, short message service (SMS), and Internet access at broadband speeds.
Most carriers also expect consumers to want :-
  location services
  interactive gaming
  streaming video
  home monitoring and control
  and who knows what else, while being fully mobile anywhere in the world.
education for life www.rimt.ac.in

## Slide 5: 3G Capabilities
Voice quality comparable to the public switched telephone network
144 Kbps- user in high-speed motor vehicles
384 Kbps- pedestrians standing or moving slowly over small areas
Up to 2 Mbps- fixed applications like office use
Symmetrical/asymmetrical data transmission rates
Support for both packet switched and circuit switched data services like Internet Protocol (IP) traffic and real time video
education for life www.rimt.ac.in

## Slide 6: Organizations
  3G is also known as UMTS (Universal Mobile Telecommunication System)
  3GPP 3rd Generation Partnership Project.
  3GPP2 3rd Generation Partnership Project 2
  Internet Engineering Taskforce (IETF)
  ITU-IMT-2000 Standard (International Telecommunication Union- International Mobile Telecommunication)
education for life www.rimt.ac.in

## Slide 7: IMT-2000 Radio Interface
IMT-DS
UMTS-FDD
(WCDMA)
Direct spread
IMT-MC
CDMA-2000
(1x-EvDO/DV)
Multi carrier
IMT-TC
UMTS-TDD
(TD-SCDMA)
Time code
IMT-SC
UWC-136
(EDGE)
Single carrier
IMT-FT
DECT
Freq. time
CDMA TDMA FDMA
I M T
Paired Spectrum
Unpaired Spectrum
education for life www.rimt.ac.in

## Slide 8: IMT-2000 Frequency Bands
1G + 2G
806
960 MHz
2G (Asia, Europe) + 3G
1710
1885 MHz
DECT, PHS + 2G + 3G
1885
2025
2110
2200 MHz
2500
2690 MHz
WCDMA(UL) 1820-1880MHz
WCDMA(DL) 1910-1970MHz
education for life www.rimt.ac.in

## Slide 9: Technologies
3G is superior to the other digital standards like:-
  GSM (Global System for Mobile) communications standard used worldwide
  And IS-136 TDMA standard used primarily in North America.
3G Technologies:-
  WCDMA or UMTS-FDD (Universal Mobile Telecommunications System - Frequency Division Duplex)---Direct Spread
  CDMA2000 - 1x-EvDO/EvDV---Multi carrier
  UMTS – TDD (Time Division Duplex) or TD-SCDMA (Time Division - Synchronous Code Division Multiple Access) ---Time Code
4G Technologies:-
  Digital Audio Broadcast (DAB) and Digital Video Broadcast (DVB) for wide area broadcasting
  Local Multipoint Distribution System (LMDS)
  Microwave Multipoint Distribution System (MMDS)
education for life www.rimt.ac.in

## Slide 10: Wireless Technologies (Figure)
education for life www.rimt.ac.in

## Slide 11: Evolution Paths
2.5G
2G
3G
cdmaOne
IS-95A
TDMA
cdmaOne
IS-95B
Cdma2000 1X
Cdma2000
1xEV-DV
Cdma2000
1xEV-DO
GSM
GPRS
EDGE
WCDMA
GSM Map Core Network
IS-41 Core Network
education for life www.rimt.ac.in

## Slide 12: Topics to be covered in next lecture
wireless local loop (WLL)
education for life www.rimt.ac.in