## Slide 1: COMPUTER ARCHITECTURE BTCS-2301
Department of Computer Science & Engineering
Prepared by: Sahilpreet Singh
Course Name: B.Tech(CSE) Semester: 3rd
education for life www.rimt.ac.in

## Slide 2: TOPIC:- PIPELINING
education for life www.rimt.ac.in

## Slide 3: Pipelining
One way to speed up CPU is to increase clock rate
  limitations on how fast clock can run to complete instruction
Another way is to execute more than one instruction at one time
education for life www.rimt.ac.in

## Slide 4: Pipelining
Pipelining breaks instruction execution down into several stages
  put registers between stages to “buffer” data and control
  execute one instruction
  as first starts second stage, execute second instruction, etc.
  speedup same as number of stages as long as pipe is full
education for life www.rimt.ac.in

## Slide 5: Pipelining (continued)
Consider an example with 6 stages
  FI = fetch instruction
  DI = decode instruction
  CO = calculate location of operand
  FO = fetch operand
  EI = execute instruction
  WO = write operand (store result)
education for life www.rimt.ac.in

## Slide 6: Pipelining Example
Executes 9 instructions in 14 cycles rather than 54 for sequential execution
education for life www.rimt.ac.in

## Slide 7: Pipelining (continued)
Hazards to pipelining
  conditional jump
    instruction 3 branches to instruction 15
    pipeline must be flushed and restarted
  later instruction needs operand being calculated by instruction still in pipeline
    pipeline stalls until result ready
education for life www.rimt.ac.in

## Slide 8: Pipelining Problem Example
Is this really a problem?
education for life www.rimt.ac.in

## Slide 9: Real-life Problem
Not all instructions execute in one clock cycle
  floating point takes longer than integer
  fp divide takes longer than fp multiply which takes longer than fp add
  typical values
    integer add/subtract 1
    memory reference 1
    fp add 2 (make 2 stages)
    fp (or integer) multiply 6 (make 2 stages)
    fp (or integer) divide 15
Break floating point unit into a sub-pipeline
  execute up to 6 instructions at once
education for life www.rimt.ac.in

## Slide 10: Pipelining (continued)
This is not simple to implement
  note all 6 instructions could finish at the same time!!
education for life www.rimt.ac.in

## Slide 11: More Speedup
Pipelined machines issue one instruction each clock cycle
  how to speed up CPU even more?
Issue more than one instruction per clock cycle
education for life www.rimt.ac.in