## Slide 1: COMPUTER ARCHITECTURE BTCS-2301
Department of Computer Science & Engineering
Prepared by: Sahilpreet Singh
Course Name: B.Tech (CSE) Semester: 3rd
education for life www.rimt.ac.in

## Slide 2: TOPIC:- BUS TYPES
education for life www.rimt.ac.in

## Slide 3: Bus Types Dedicated vs. Time Multiplexed
Dedicated
  Separate data & address lines
Time multiplexed
  Shared lines
  Address valid or data valid control line
  Advantage - fewer lines
  Disadvantages
    More complex control
    Degradation of performance
education for life www.rimt.ac.in

## Slide 4: Bus Types Physical Dedication
  Physically separating buses and controlling them with a "channel changer“
  Advantages – faster
  Disadvantages – physically larger
education for life www.rimt.ac.in

## Slide 5: Bus Arbitration
Listening to the bus is not usually a problem
Talking on the bus is a problem – need arbitration to allow more than one module to control the bus at one time
Arbitration may be centralised or distributed
education for life www.rimt.ac.in

## Slide 6: Centralised vs. Distributed Arbitration
Centralised Arbitration
  Single hardware device controlling bus access – Bus Controller/Arbiter
  May be part of CPU or separate
Distributed Arbitration
  Each module may claim the bus
  Access control logic is on all modules
  Modules work together to control bus
education for life www.rimt.ac.in

## Slide 7: Bus Timing
Co-ordination of events on bus
Synchronous – controlled by a clock
Asynchronous – timing is handled by well-defined specifications, i.e., a response is delivered within a specified time after a request
education for life www.rimt.ac.in

## Slide 8: Synchronous Bus Timing
Events determined by clock signals
Control Bus includes clock line
A single 1-0 cycle is a bus cycle
All devices can read clock line
Usually sync on leading/rising edge
Usually a single cycle for an event
Analogy – Orchestra conductor with baton
Usually stricter in terms of its timing requirements
education for life www.rimt.ac.in

## Slide 9: Synchronous Bus Timing
education for life www.rimt.ac.in

## Slide 10: Asynchronous Timing
Devices must have certain tolerances to provide responses to signal stimuli
More flexible allowing slower devices to communicate on same bus with faster devices.
Performance of faster devices, however, is limited to speed of bus
education for life www.rimt.ac.in

## Slide 11: Asynchronous Timing – Read
education for life www.rimt.ac.in

## Slide 12: Asynchronous Timing – Write
education for life www.rimt.ac.in

## Slide 13: Bus Width
Wider the bus the better the data transfer rate or the wider the addressable memory space
Serial “width” is determined by length/duration of frame
education for life www.rimt.ac.in