## Slide 1: ELEMENTS OF MECHANICAL ENGINEERING(BMEC-1201)
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Prepared by: Dr. Sachin Saini
Course Name: ELEMENTS OF MECHANICAL ENGINEERING(BMEC-1201) Semester: 2nd

## Slide 2: IC ENGINES
CLASSIFICATION OF IC ENGINES
DIFFERENTIATING IC ENGINES
DIFFERENCE BETWEEN PETROL AND DIESEL ENGINES
CONSTRUCTIONAL FEATURES OF IC ENGINES
COMPARISON BETWEEN PETROL AND DIESEL ENGINES
education for life www.rimt.ac.in
Department of Computer Science & Engineering

## Slide 3: Construction and Working of IC Engine
education for life www.rimt.ac.in
Department of Computer Science & Engineering

## Slide 4: Classification of IC Engines
education for life www.rimt.ac.in
Department of Computer Science & Engineering
types of heat engines
external combustion
internal combustion
steam engines
Stirling engine
Otto engine
Diesel engine
Vankel engine

## Slide 5: Parts of IC Engine
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Spark plug
Piston
Piston rings
Intake valve
Crankshaft
Cylinder
Piston rod
Exhaust valve

## Slide 6: Working of IC Engine
INTAKE STROKE:
education for life www.rimt.ac.in
Department of Computer Science & Engineering
This starts at the highest point known as top dead centre and ends at bottom dead centre
The intake stroke allows the piston to suck fuel and air into the combustion chamber through the intake valve port.

## Slide 7: COMPRESSION STROKE
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Compression starts at bottom dead centre and ends at top dead centre.
The second motion of the stroke takes all the fuel and air that was stored and compresses it into one tenth its original sizes. Making the air/fuel mixture increase in temperature preparing it for the next stage in its combustion cycle.

## Slide 8: POWER STROKE
education for life www.rimt.ac.in
Department of Computer Science & Engineering
The power stroke starts as soon as the piston reaches top dead centre allowing the spark plug to ignite.
This electric current created by the spark plug ignites the fuel and air mixture sending the piston back down the cylinder with a pressure reaching high as 600 PSI.

## Slide 9: EXHAUST STROKE
education for life www.rimt.ac.in
Department of Computer Science & Engineering
The final stage of the stroke releases all the burned fuel through the exhaust valve.
As the piston moves from bottom dead center to top dead center it takes all the burned fuel and pushes it out of the cylinder, preparing it for the next cycle of strokes.

## Slide 10: SCHEMATIC SKETCH
education for life www.rimt.ac.in
Department of Computer Science & Engineering

## Slide 11: DIESEL ENGINES
Diesel engines work on the same principle as the two and four stroke engines. They do not need a spark plug to ignite the fuel. During the intake stroke, air does not mixed with the fuel in the cylinder. Instead as the air reaches high enough compression Fuel is then sprayed into the cylinder creating ignition. This pushes the piston down the cylinder at a pressure of 500 PSI, starting the stroke all over again.
education for life www.rimt.ac.in
Department of Computer Science & Engineering

## Slide 12: WORKING OF DIESEL ENGINE
education for life www.rimt.ac.in
Department of Computer Science & Engineering

## Slide 13: WORKING OF DIESEL ENGINE
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Induction Stroke
The induction stroke in a Diesel engine is used to draw in a new volume of charge air into the cylinder. As the power generated in an engine is dependent on the quantity of fuel burnt during combustion and that in turn is determined by the volume of air (oxygen) present, most diesel engines use turbochargers to force air into the cylinder during the induction stroke.
Compression Stroke
The compression stroke begins as the inlet valve closes and the piston is driven upwards in the cylinder bore by the momentum of the crankshaft and flywheel.
The purpose of the compression stroke in a Diesel engine is to raise the temperature of the charge air to the point where fuel injected into the cylinder spontaneously ignites. In this cycle, the separation of fuel from the charge air eliminates problems with auto-ignition and therefore allows Diesel engines to operate at much higher compression ratios than those currently in production with the Otto Cycle.
Power Stroke
The power stroke begins as the injected fuel spontaneously ignites with the air in the cylinder. As the rapidly burning mixture attempts to expand within the cylinder walls, it generates a high pressure which forces the piston down the cylinder bore. The linear motion of the piston is converted into rotary motion through the crankshaft. The rotational energy is imparted as momentum to the flywheel which not only provides power for the end use, but also overcomes the work of compression and mechanical losses incurred in the cycle (valve opening and closing, alternator, fuel injector pump, water pump, etc.).
Exhaust Stroke
The exhaust stroke is as critical to the smooth and efficient operation of the engine as that of induction. As the name suggests, it's the stroke during which the gases formed during combustion are ejected from the cylinder. This needs to be as complete a process as possible, as any remaining gases displace an equivalent volume of the new charge air and leads to a reduction in the maximum possible power.

## Slide 14: COMPARISON BETWEEN DIESEL AND PETROL ENGINES
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Higher thermal efficiency as a consequence of a higher compression ratio (16-20 vs 9-12) needed for the self ignition of the mixture
Higher efficiency at part load condition (city driving) because of the different load control with much inferior pumping loss for aspirating air into the cylinder: load control directly by varying the fuel delivery, while in the Otto engine by varying the air through an intake throttle
Less energy spent to produce Diesel fuel
Higher weight for same power delivery, because of higher thermal and mechanical stresses due to higher temperatures and pressures , almost double vs Otto engine, at the end of compression and combustion phases
Lower maximum engine speed because a slower combustion process and higher weight of the rotating an oscillating masses
Engine roughness that generates higher structural and airborne vibration/noise.
Advantages
Disadvantages

## Slide 15: TWO STROKE CYCLE
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Two-stroke cycle
Gas exchange occurs between the working cycles by scavenging the exhaust gases with a fresh cylinder charge
Control mostly via intake end exhaust ports
In contrast to the four-stroke cycle , no valve train is necessary, but a blower is need for scavenging air

## Slide 16
WORKING OF TWO STROKE ENGINES:
education for life www.rimt.ac.in
Department of Computer Science & Engineering
2-StrokeEngines

## Slide 17: COMPARISON B/W 4-S AND 2-S CYCLES
education for life www.rimt.ac.in
Department of Computer Science & Engineering
4-stroke engine
High volumetric efficiency over a wide engine speed range
Low sensitivity to pressure losses in the exhaust system
Effective control of the charging efficiency trough appropriate valve timing and intake system design
2-stroke engine
Very simple and cheap engine design
Low weight
Low manufacturing cost
Better torsional forces pattern
2-stroke engine
Higher fuel consumption
Higher HC emissions because of a problematic cylinder scavenging
Lower mean effective pressure because of poorer volumetric efficiency
Higher thermal load because no gas echange stroke
Poor idle because of high residual gas percentage into the cylinder
4-stroke engine
High complexity of the valve control
Reduced power density because the work is generated only every second shaft rotation
Advantages
Disdvantages

## Slide 18: FOUR STROKE VS TWO STROKE ENGINES
FOUR STROKE ENGINES
ADVANTAGES
High torque output
Smooth running
Quieter operation
Lower emissions output
Higher horse power availability
Heavier construction
No Gas/Oil mixing
DISADVANTAGES
Heavy
Limited slope operation
More moving parts
education for life www.rimt.ac.in
Department of Computer Science & Engineering
TWO STROKE ENGINES
ADVANTAGES
Lighter
Can be operated in all positions
Less moving parts
Higher horse power per cc displacement
DISADVANTAGES
Low torque output
Erratic running Characteristic
Noisy
Higher emissions output
Gas/Oil mixing

## Slide 19: Summary
Internal combustion engines have ultimately revolutionized the lives
With the small and light weight design of the two cycle engine tasks like trimming the hedges and cutting down weeds became easier and more efficient. With the power of the four stroke we are now able to dig up dirt and cut down trees with out even breaking a sweat. Internal combustion engines have made life easier since the first one was built in the early 1800’s.
education for life www.rimt.ac.in
Department of Computer Science & Engineering

## Slide 20: Topics to be Discussed in Next Lecture
Introduction to the topic of Machines and their usage
Various types of Links and mechanisms
Differentiating between Constrained and incompletely constrained motions
Different types of Inversions
education for life www.rimt.ac.in
Department of Computer Science & Engineering