## Slide 1: Strength of Materials-I(BMEC-2301)
education for life www.rimt.ac.in
Department of Mechanical Engineering
Prepared by: Ajay Singh Rana
Course Name: B.Tech-Mechanical Semester: 3rd

## Slide 2
education for life www.rimt.ac.in
Department of Mechanical Engineering
Torsion

## Slide 3: Topic Discussed
education for life www.rimt.ac.in
Department of Mechanical Engineering
Torsion of Shaft
Angle of Twist
Derivation of Torsional Equation
Power Transmitted by shaft
Strength of hollow shaft
Polar Moment of Inertia
Numerical

## Slide 4: TORSION OF CIRCULAR SHAFT
TOROUE OR TURNING MOMENT OR TWISTING MOMENT :-
In factories and workshops, shafts is used to transmit energy from one end to other end.
To transmit the energy, a turning force is applied either to the rim of a pulley, keyed to the shaft is, or to any other suitable point at some distance from the axis of the shaft.
The moment of couple acting on the shaft is called torque or turning moment or twisting moment.

## Slide 5
education for life www.rimt.ac.in
Department of Mechanical Engineering
Torque = turning force x diameter of shaft
T = F x 2R
where :
T=Torque
F=Turning force
S=Radius of the shaft
Unit of Torque(T) is N.mm or kN.mm

## Slide 6: When the shaft is subjected to Torque (T),point A on the surface of the shaft comes to A’ position. The angle AOA’ at the centre of the shaft is called the angle of twist.
education for life www.rimt.ac.in
Department of Mechanical Engineering
A0A’= =Angle of twist
< Angle of twist is measured in radians.

## Slide 7
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 8
education for life www.rimt.ac.in
Department of Mechanical Engineering
  The following assumptions are made while finding out shear stress in a circular
shaft subjected to torsion.
The material of shaft is uniform throughout the length.
The twist along the shaft is uniform.
The shaft is of uniform circular section throughout the length.
Cross section of the shaft, which are plane before twist remain plane after
twist.
All radii which are straight before twist remain straight after twist.

## Slide 9
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 10
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 11
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 12
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 13
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 14
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 15
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 16
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 17
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 18
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 19
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 20
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 21
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 22
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 23
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 24
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 25
education for life www.rimt.ac.in
Department of Mechanical Engineering