## Slide 1: DIGITAL ELECTRONICS &LOGIC DESIGN
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Prepared by: Er. Irfana Shafi
Course Name: B.Tech CSE Semester: 3rd

## Slide 2
UNIT 1
INTRODUCTION TO DIGITAL LOGIC DESIGN
2

## Slide 3: INTRODUCTION TO DIGITAL LOGIC DESIGN
Digital logic design is a system in electrical and computer engineering that uses simple number values to produce inpuand output operations.
3
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Advantages:
A digital computer stores data in terms of digits (numbers) and proceeds in discrete steps from one state to the next.
The states of a digital computer typically involve binary digits which may take the form of the presence or absence of magnetic markers in a storage medium , on- off switches or relays. In digital computers, even letters, words and whole texts are represented digitally.

## Slide 4: NUMBER SYSTEMS
4
education for life www.rimt.ac.in
Department of Computer Science & Engineering

## Slide 5: NUMBER BASE CONVERSION
5
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Binary to Decimal Conversion:
It is by the positional weights method . In this method each binary digit of the no. is multiplied by its position weight . The product terms are added to obtain the decimal no.
Example : Convert the binary number 10100011 to decimal.
Solution:
Given binary number is 10100011
Using the conversion formula,
10100011 = (1 × 27) + (0 × 26) + (1 × 25) + (0 × 24) + (0 × 23) + (0 × 22) + (1 × 21) + (1 × 20)
= 128 + 0 + 32 + 0 + 0 + 0 + 2 + 1
= 163
Therefore, binary number 10100011 = 163 decimal number

## Slide 6: NUMBER BASE CONVERSION
6
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Binary to Octal conversion:
Starting from the binary pt. make groups of 3 bits each, on either side of the binary pt, & replace each 3 bit binary group by the equivalent octal digit.
Example 1: Convert 10101012 to octal
Solution:
Given binary number is 10101012
First, we convert given binary to decimal
1010101210101012 = (1 * 26) + (0 * 25 ) + (1 * 24) + (0 * 23) + (1 * 22) + (0 * 21) + (1 * 20)
= 64 + 0 + 16 + 0 + 4 + 0 + 1
= 64 + 21
0101012= 85 (Decimal form)
Now we will convert this decimal to octal form
Therefore, the equivalent octal number is 1258

## Slide 7: NUMBER BASE CONVERSION
7
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Binary to Hexadecimal conversion:
For this make groups of 4 bits each , on either side of the binary pt & replace each 4 bit group by the equivalent hexadecimal digit.

## Slide 8: NUMBER BASE CONVERSION
8
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Decimal to Binary conversion:
Method: is for small no.s The values of various powers of 2 need to be remembered. for conversion of larger no.s have a table of powers of 2 known as the sum of weights method. The set of binary weight values whose sum is equal to the decimal no. is determined.
II.Method : It converts decimal integer no. to binary integer no by successive division by 2 & the decimal fraction is converted to binary fraction by double –dabble method

## Slide 9: NUMBER BASE CONVERSION
9
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Octal to decimal Conversion:
Multiply each digit in the octal no by the weight of its position&add all the product terms Decimal value of the octal no.
Example
Convert Octal number 2671 to a Decimal number.
Solution:
(2671)8 = 2 × 83 + 6 × 82 + 7 × 81 + 1 × 80
(2671)8 = 2 × 512 + 6 × 64 + 7 × 8 + 1 × 1
(2671)8 = 1024 + 384 + 56 + 1
(2671)8 = 1465
Therefore, (2671)8 = (1465)10.

## Slide 10: NUMBER BASE CONVERSION
10
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Decimal to Octal Conversion:
There are two methods of converting decimals to octals:
1. Convert Decimal to Binary to Octal
2. Convert Decimal to Octal
Method 1: Convert Decimal to Binary to Octal
In this method, we first find the binary equivalent of the given number. Once the binary number is obtained, we convert it into an octal number

## Slide 11: NUMBER BASE CONVERSION
11
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Example
Convert decimal number 98 into octal number.
First convert it into binary or hexadecimal number,
= (98)10
= (1x26+1x25+0x24+0x23+0x22+1x21+0x20)10
= (1100010)2
2. convert each group of 3 bits from least significant of binary number.
= (001 100 010)2
= (001 100 010)2
= (1 4 2)8 = (142)8

## Slide 12: NUMBER BASE CONVERSION
12
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Decimal to Hexadecimal conversion:
It is successively divide the given decimal no. by 16 till the quotient is zero. The last remainder is the MSB. The remainder read from bottom to top gives the equivalent hexadecimal integer. To convert a decimal fraction to hexadecimal successively multiply the given decimal fraction & subsequent decimal fractions by 16, till the product is zero. Or till the required accuracy is obtained , and collect all the integers to the left of decimal pt. The first integer is MSB & the integer read from top to bottom give the hexadecimal fraction known as the hexa dabble method.

## Slide 13: NUMBER BASE CONVERSION
13
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Decimal to Hexadecimal conversion:
Convert decimal number 105 into hexadecimal number.
First convert it into binary or octal number,
= (100)10
= (1x26+1x25+0x24+0x23+1x22+0x21+0x20)10 or (1x82+4x81+4x80)10
Because base of binary and octal are 2 and 8 respectively.
= (1100100)2 or (144)8 Then convert each digit of octal number into 3 bit of binary number, then use grouping of 4 bit of binary number.
= (1100100)2
or (001 100 100)2
= (110 0100)2
= (0110 0100)2
= (6 4)16
= (64)16

## Slide 14: NUMBER BASE CONVERSION
14
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Octal to hexadecimal conversion:
The simplest way is to first convert the given octal no. to binary & then the binary no. to hexadecimal.

## Slide 15: NUMBER BASE CONVERSION
15
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Octal to hexadecimal conversion:
Example :
Convert 536 from octal to hexadecimal number
Convert 536(octal) into its binary equivalent we get ( 536)8 = (101) (011) (110) =(101011110)2 2. Now forming the group of 4 binary bits to obtain its hexadecimal equivalent, (101011110)2
= (0001) (0101) (1110) = (15E)16
So the hexadecimal number of 536 is 15E.

## Slide 16: FINDING THE BASE OF THE NUMBERSYSTEM
16
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Find r such that (121)r=(144)8, where r and 8 are the bases
1*82 + 4*8+4*8 = 64+32+4 =100
1*r2+2*r+1*r0 = r2+2r+1=(r+1)2
(r+1)2=100
r+1=10
r=9