## Slide 1: DIGITAL ELECTRONICS &LOGIC DESIGN
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Prepared by: Er. Irfana Shafi
Assistant Professor :Electrical Engineering Department
Course Name: B.Tech CSE Semester: 3rd

## Slide 2: BINARY ARITHMETIC
2
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Binary Addition:
Rules:
0+0=0
0+1=1
1+0=1
1+1=10
i.e, 0 with a carry of 1.

## Slide 3: BINARY ARITHMETIC
3
.
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Binary Subtraction:
Rules:
0-0=0
1-1=0
1-0=1
0-1=1 with a borrow of 1

## Slide 4: BINARY ARITHMETIC
4
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Binary multiplication:
Rules:
0x0=0
1x1=0
1x0=0
0x1=0

## Slide 5
5
.
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Binary multiplication:
Rules:
0x0=0
1x1=0
1x0=0
0x1=0
BINARY ARITHMETIC

## Slide 6: BINARY ARITHMETIC
Binary Division:
Example : 1011012 by 110
110 ) 101101 ( 111.1
110
1010
110
1001
110
110
110
000
6
Ans:
111.1
education for life www.rimt.ac.in
Department of Computer Science & Engineering

## Slide 7: BINARY ARITHMETIC
7
education for life www.rimt.ac.in
Department of Computer Science & Engineering
9’s & 10’s Complements:
It is the Subtraction of decimal no.s can be accomplished by the 9’s & 10’s compliment methods similar to the 1’s & 2’s compliment methods of binary . the 9’s compliment of a decimal no. is obtained by subtracting each digit of that decimal no. from 9. The 10’s compliment of a decimal no is obtained by adding a 1 to its 9’s compliment.

## Slide 8: BINARY ARITHMETIC
8
education for life www.rimt.ac.in
Department of Computer Science & Engineering
1’s compliment of n number:
It is obtained by simply complimenting each bit of the no,.& also , 1’s comp of a no, is subtracting each bit of the no. form 1.This complemented value rep the –ve of the original no. One of the difficulties of using 1’s comp is its rep o f zero. Both 00000000 & its 1’s comp 11111111 rep zero. The 00000000 called +ve zero& 11111111 called –ve zero.

## Slide 9: BINARY ARITHMETIC
9
education for life www.rimt.ac.in
Department of Computer Science & Engineering
1’s compliment arithmetic:
In 1’s comp subtraction, add the 1’s comp of the subtrahend to the minuend. If there is a carryout , bring the carry around & add it to the LSB called the end around carry. Look at the sign bit (MSB) . If this is a 0, the result is +ve & is in true binary. If the MSB is a 1 ( carry or no carry ), the result is –ve & is in its is comp form .Take its 1’s comp to get the magnitude in binary

## Slide 10: BINARY ARITHMETIC
10
.
education for life www.rimt.ac.in
Department of Computer Science & Engineering
9’s & 10’s Complements:
It is the Subtraction of decimal no.s can be accomplished by the 9’s & 10’s compliment methods similar to the 1’s & 2’s compliment methods of binary . the 9’s compliment of a decimal no. is obtained by subtracting each digit of that decimal no. from 9. The 10’s compliment of a decimal no is obtained by adding a 1 to its 9’s compliment

## Slide 11: BINARY ARITHMETIC
11
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Methods of obtaining 2’s comp of a no:
In 3 ways
1. By obtaining the 1’s comp of the given no. (by changing all 0’s to1’s & 1’s to 0’s) & then adding 1.
2. By subtracting the given n bit no N from 2n
3. Starting at the LSB , copying down each bit upto & including the first 1 bit encountered , and complimenting the remaining bits.

## Slide 12: BINARY ARITHMETIC
12
education for life www.rimt.ac.in
Department of Computer Science & Engineering
2’s compliment Arithmetic:
The 2’s comp system is used to rep –ve no.s using modulus arithmetic . The word length of a computer is fixed. i.e, if a 4 bit no. is added to another 4 bit no . the result will be only of 4 bits. Carry if any , from the fourth bit will overflow called the Modulus arithmetic.
Ex:1100+1111=1011

## Slide 13: BINARY ARITHMETIC
13
education for life www.rimt.ac.in
Department of Computer Science & Engineering
9’s & 10’s Complements:
It is the Subtraction of decimal no.s can be accomplished by the 9’s & 10’s compliment methods similar to the 1’s & 2’s compliment methods of binary . The 9’s compliment of a decimal no. is obtained by subtracting each digit of that decimal no. from 9. The 10’s compliment of a decimal no is obtained by adding a 1 to its 9’s compliment

## Slide 14
14
education for life www.rimt.ac.in
Department of Computer Science & Engineering
9’s & 10’s Complements:
It is the Subtraction of decimal no.s can be accomplished by the 9’s & 10’s compliment methods similar to the 1’s & 2’s compliment methods of binary . the 9’s compliment of a decimal no. is obtained by subtracting each digit of that decimal no. from9. The 10’s compliment of a decimal no is obtained by adding a 1 to its 9’s compliment
BINARY ARITHMETIC

## Slide 15: BINARY WEIGHTED AND NON- WEIGHTED CODES
15
.
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Weighted Codes:-
The weighted codes are those that obey the position weighting principle, which states that the position of each number represent a specific weight. In these codes each decimal digit is represented by a group of four bits.
In weighted codes, each digit is assigned a specific weight according to its position. For example, in 8421/BCD code, 1001 the weights of 1, 1, 0, 1 (from left to right) are 8, 4, 2
and 1 respectively.
Examples: 8421,2421 are all weighted codes.

## Slide 16: BINARY WEIGHTED AND NON- WEIGHTED CODES
16
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Non-weightedcodes:
The non-weighted codes are not positionally weighted . In other words codes that are not assigned with any weight to each digit position.
Examples:Excess-3(XS-3) and Gray Codes.

## Slide 17: BINARY CODED DECIMAL
17
education for life www.rimt.ac.in
Department of Computer Science & Engineering
BCD Addition:
It is individually adding the corresponding digits of the decimal no,s expressed in 4 bit binary groups starting from the LSD . If there is no carry & the sum term is not an illegal code , no correction is needed. If there is a carry out of one group to the next group or if the sum term is an illegal code then 610(0100) is added to the sum term of that group & the resulting carry is added to the next group.
.

## Slide 18: BINARY CODED DECIMAL
18
education for life www.rimt.ac.in
Department of Computer Science & Engineering
BCD Subtraction:
Performed by subtracting the digits of each 4 bit groupof the subtrahend the digits from the corresponding 4- bit group of the minuend in binary starting from the LSD . if there is no borrow from the next group , then 610(0110)is subtracted from the difference term of this group.

## Slide 19: BINARY CODED DECIMAL
19
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Excess-3Addition:
Add the xs-3 no.s by adding the 4 bit groups in each column starting from the LSD. If there is no carry starting from the addition of any of the 4-bit groups , subtract 0011 from the sum term of those groups ( because when 2 decimal digits are added in xs-3 & there is no carry , result in xs-6). If there is a carry out, add 0011 to the sum term of those groups( because when there is a carry, the invalid states are skipped and the result is normal binary).

## Slide 20: BINARY CODED DECIMAL
20
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Excess -3 (XS-3) Subtraction:
Subtract the xs-3 no.s by subtracting each 4 bit group of the subtrahend from the corresponding 4 bit group of the minuend starting form the LSD .if there is no borrow from the next 4-bit group add 0011 to the difference term of such groups (because when decimal digits are subtracted in xs-3 & there is no borrow
, result is normal binary). I f there is a borrow , subtract 0011 from the difference term(b coz taking a borrow is equivalent to adding six invalid states , result is in xs-6)

## Slide 21: BINARY CODED DECIMAL
21
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Representation of signed no.s binary arithmetic in computers:
T w o ways of represent signed no.s
Sign Magnitude form
Complemented form
Two complimented forms
1’s compliment form
2’s compliment form

## Slide 22: BINARY CODED DECIMAL
22
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Error – Detecting codes:
When binary data is transmitted & processed, it is susceptible to noise that can alter or distort its contents. The 1’s may get changed to 0’s & 1’s .because digital systems must be accurate to the digit, error can pose a problem. Several schemes have been devised to detect the occurrence of a single bit error in a binary word, so that whenever such an error occurs the concerned binary word can be corrected & retransmitted.