## Slide 1: DIGITAL ELECTRONICS &LOGIC DESIGN
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Prepared by: Er. Irfana Shafi
Course Name: B.Tech CSE Semester: 3rd

## Slide 2: BINARY CODED DECIMAL
2
.
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Error – Detecting codes:
When binary data is transmitted & processed, it is susceptible to noise that can alter or distort its contents. The 1’s may get changed to 0’s & 1’s .because digital systems must be accurate to the digit, error can pose a problem. Several schemes have been devised to detect the occurrence of a single bit error in a binary word, so that whenever such an error occurs the concerned binary word can be corrected & retransmitted.

## Slide 3: ERROR DETECTING AND CORRECTING CODES
3
.
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Introduction:
  When we talk about digital systems, be it a digital computer or a digital communication set-up, the issue of error detection and correction is of great practical significance.
  Errors creep into the bit stream owing to noise or other impairments during the course of its transmission from the transmitter to the receiver.
  While the addition of redundant bits helps in achieving the goal of making transmission of information from one place to another error free or reliable, it also makes it inefficient.

## Slide 4: ERROR DETECTING AND CORRECTING CODES
4
.
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Some Common Error Detecting and Correcting Codes
  Parity Code
  Repetition Code
  Cyclic Redundancy Check Code
  Hamming Code

## Slide 5: ERROR DETECTING AND CORRECTING CODES
5
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Parity Code:
A parity bit is an extra bit added to a string of data bits in order to detect any error that might have crept into it while it was being stored or processed and moved from one place to another in a digital system.
This simple parity code suffers from two limitations. Firstly, it cannot detect the error if the number of bits having undergone a change is even.
Repetition Code:
The repetition code makes use of repetitive transmission of each data bit in the bit stream. In the case of threefold repetition, ‘1’ and ‘0’ would be transmitted as ‘111’ and ‘000’ respectively.
The repetition code is highly inefficient and the information throughput drops rapidly as we increase the number of times each data bit needs to be repeated to build error detection and correction capability.

## Slide 6: ERROR DETECTING AND CORRECTING CODES
6
.
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Cyclic Redundancy Check Code:
  Cyclic redundancy check (CRC) codes provide a reasonably high level of protection at low redundancy level.
  The probability of error detection depends upon the number of check bits, , used to construct the cyclic code. It is 100 % for single-bit and two- bit errors. It is also 100 % when an odd number of bits are in error and the error bursts have a length less than n + 1 .

## Slide 7: ERROR DETECTING AND CORRECTING CODES
7
.
education for life www.rimt.ac.in
Department of Computer Science & Engineering
Hamming Code:
  An increase in the number of redundant bits added to message bits can enhance the capability of the code to detect and correct errors.
  If sufficient number of redundant bits arranged such that different error bits produce different error results, then it should be possible not only to detect the error bit but also to identify its location.
  In fact, the addition of redundant bits alters the ‘distance’ code parameter,
which has come to be known as the Hamming distance.
Hamming Distance:
  The Hamming distance is nothing but the number of bit disagreements
between two code words.

## Slide 8: ERROR DETECTING AND CORRECTING CODES
8
.
education for life www.rimt.ac.in
Department of Computer Science & Engineering
For example, the addition of single-bit parity results in a code with a
Hamming distance of at least 2.
The smallest Hamming distance in the case of a threefold repetition code
would be 3.
Hamming noticed that an increase in distance enhanced the code’s ability to detect and correct errors.
Hamming’s code was therefore an attempt at increasing the Hamming distance and at the same time having as high an information throughput rate as possible.

## Slide 9: ERROR DETECTING AND CORRECTING CODES
9
.
education for life www.rimt.ac.in
Department of Computer Science & Engineering
The Hamming code is capable of correcting single-bit errors on messages of
any length.
Although the Hamming code can detect two-bit errors, it cannot give the error
locations.
The number of parity bits required to be transmitted along with the message, however, depends upon the message length.
The number of parity bits n required to encode m message bits is the smallest integer that satisfies the condition .
The most commonly used Hamming code is the one that has a code word length of seven bits with four message bits and three parity bits.
It is also referred to as the Hamming (7, 4) code

## Slide 10: ERROR DETECTING AND CORRECTING CODES
The code word sequence for this code is written as P1P2D1P3D2D3D4, with P1, P2 and P3 being the parity bits and D1, D2, D3 and D4 being the data bits.
Generation of Hamming Code:
10
education for life www.rimt.ac.in
Department of Computer Science & Engineering