## Slide 1: INDUSTRIAL AUTOMATION AND ROBOTICS(BTME-3505)
education for life www.rimt.ac.in
Department of Mechanical Engineering
Prepared by: Dr. Sachin Saini
Course Name: IAR Semester: 5th

## Slide 2: Introduction to Automation
education for life www.rimt.ac.in
Department of Mechanical Engineering
AUTOMATION IN PRODUCTION SYSTEMS Automation can be defined as a technology concerned with the application of mechanical, electronic, and computer based systems to operate and control production. The automated elements of the production system can be separated into two categories:
automation of the manufacturing systems in the factory and (2) computerization of the manufacturing support systems.
Types of Automation:
(1) fixed automation, (2) programmable automation, and (3) flexible automation.
Fixed Automation. Fixed automation is a system in which the sequence of processing (or assembly) operations is fixed by the equipment configuration. Each of the operations in the sequence is usually simple, involving perhaps a plain linear or rotational motion or an uncomplicated combination of the two; for example, the feeding of a rotating spindle. It is the integration and coordination of many such operations into one piece of equipment that makes the system complex. Typical features of fixed automation are: • high initial investment for custom engineered equipment • high production rates • relatively inflexible in accommodating product variety

## Slide 3: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
Programmable Automation. In programmable automation, the production equipment is designed with the capability to change the sequence of operations to accommodate different product configurations. The operation sequence is controlled by a program, which is a set of instructions coded so that they can be read and interpreted by the system. New programs can be prepared and entered into the equipment to produce new products. Some of the features that characterize programmable automation include: • high investment in general purpose equipment • lower production rates than fixed automation • flexibility to deal with variations and changes in product configuration • most suitable for batch production
Programmable automated production systems are used in low and medium volume production. The parts or products are typically made in batches. To produce each new batch of a different product, the system must be reprogrammed with the set of machine instructions that correspond to the new product. The physical setup of the machine must also be changed: Tools must be loaded, fixtures must be attached to the machine table, and the required machine settings must be entered. This changeover procedure takes time. Consequently, the typical cycle for a given product includes a period during which the setup and reprogramming takes place, followed by a period in which the batch is produced. Examples of programmable automation include numerically controlled (NC) machine tools, industrial robots, and programmable logic controllers.

## Slide 4: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
Flexible Automation. Flexible automation is an extension of programmable automation. A flexible automated system is capable of producing a variety of parts (or products) with virtually no time lost for changeovers from one part style to the next. There is no lost production time while reprogramming the system and altering the physical setup (tooling, fixtures, machine settings). Consequently, the system can produce various combinations and schedules of parts or products instead of requiring that they be made in batches. What makes flexible automation possible is that the differences between parts processed by the system are not significant. It is a case of soft variety, so that the amount of changeover required between styles is minimal.
The features of flexible automation can be summarized as follows:
• high investment for a custom engineered system
• continuous production of variable mixtures of products
• medium production rates
• flexibility to deal with product design variations

## Slide 5: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
The relative positions of the three types of automation for different production volumes and product varieties are depicted in Figure 1.7. For low production quantities and new product introductions, manual production is competitive with programmable automation, as we indicate in the figure and discussed.

## Slide 6: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
Reasons for Automating Companies undertake projects in manufacturing automation and computer integrated manufacturing for a variety of good reasons. Some of the reasons used to justify automation are the following:
To increase labor productivity. Automating a manufacturing operation usually increases production rate and labor productivity. This means greater output per hour of labor input.
To reduce labor cost. Ever increasing labor cost has been and continues to be the trend in the world’s industrialized societies. Consequently, higher investment in automation has become economically justifiable to replace manual operations. Machines are increasingly being substituted for human labor to reduce unit product cost.
To mitigate the effects of labor shortages. There is a general shortage of labor in many advanced nations, and this has stimulated the development of automated operations as a substitute for labor.
To reduce or eliminate routine manual and clerical tasks. An argument can be put forth that there is social value in automating operations that are routine, boring, fatiguing, and possibly irksome. Automating such tasks serves a purpose of improving the general level of working conditions.

## Slide 7: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
5. To improve worker safety. By automating a given operation and transferring the worker from active participation in the process to a supervisory role, the work is made safer. The safety and physical wellbeing of the worker has become a national objective with the enactment of the Occupational Safety and Health Act (OSHA) in 1970. This has provided an impetus for automation.
6. To improve product quality. Automation not only results in higher production rates than manual operations; it also performs the manufacturing process with greater uniformity and conformity to quality specifications. Reduction of fraction defect rate is one of the chief benefits of automation.
7. To reduce manufacturing lead time. Automation helps to reduce the elapsed time between customer order and product delivery, providing a competitive advantage to the manufacturer for future orders. By reducing manufacturing lead time, the manufacturer also reduces work in process inventory.

## Slide 8: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
Automation Strategies include:
Specialization of operations
Combined operations
Simultaneous operations
Integration of operations
Increased flexibility
Improved material handling and storage
On- line inspection
Process control & optimization
Plan operations control
Computer-integrated manufacturing (CIM)

## Slide 9: Fluid Power Control
education for life www.rimt.ac.in
Department of Mechanical Engineering
Fluid Power is the technology that deals with the generation, control, and transmission of power, using pressurized fluids. Fluid power is called hydraulics when the fluid is a liquid and is called pneumatics when the fluid is a gas. Hydraulic systems use liquids such as petroleum oils, synthetic oils, and water. Pneumatic systems use air as the gas medium because air is very abundant and can be readily exhausted into the atmosphere after completing its assigned task.
TYPES OF FLUID POWER SYSTEM
The Fluid power system is divided in to two types. They are hydraulic and pneumatic system depends upon the fluid medium used to transmit force.
The hydraulic fluid power system employs liquid (like as water, petroleum oils and synthetic oils) as fluid medium.
The pneumatic fluid power system employs gas (Compressed Air) as the fluid medium.
COMPONENTS OF A FLUID POWER SYSTEM:
Hydraulic System: There are six basic components required in a hydraulic system:
1) A tank (reservoir) to hold the hydraulic oil.
2) A pump to force the oil through the system.
3) An electric motor or other power source to drive the pump.
4) Valves to control oil direction, pressure, and flow rate.
5) An actuator to convert the pressure of the oil into mechanical force to do the useful work.
6) Piping to carry the oil from one location to the other.

## Slide 10: Components of Hydraulic Systems:
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 11: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 12: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
Pneumatic systems have components that are similar to those used in hydraulic systems.
1) An air tank to store a given volume of compressed air.
2) A compressor to compress the air that comes directly from the atmosphere.
3) An electric motor or other prime mover to drive the compressor.
4) Valves to control air direction, pressure and flow rate.
5) Actuators, which are similar in operation to hydraulic actuators.
6) Piping to carry the pressurized air from one location to another
ADVANTAGES OF FLUID POWER SYSTEM:
The advantages of a fluid power system are as follows:
1) Fluid power systems are simple, easy to operate and can be controlled accurately: Fluid power gives flexibility to equipment without requiring a complex mechanism. Using fluid power, we can start, stop, accelerate, decelerate, reverse or position large forces/components with great accuracy using simple levers and push buttons.
2) Multiplication and variation of forces: Linear or rotary force can be multiplied by a fraction of a kilogram to several hundreds of tons.
3) Multifunction control: A single hydraulic pump or air compressor can provide power and control for numerous machines using valve manifolds and distribution systems.
.

## Slide 13: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
4) Low-speed torque: Unlike electric motors, air or hydraulic motors can produce a large amount of torque while operating at low speeds.
5) Constant force or torque: Fluid power systems can deliver constant torque or force regardless of speed changes.
6) Economical: Not only reduction in required manpower but also the production or elimination of operator fatigue, as a production factor, is an important element in the use of fluid power.
7) Low weight to power ratio: The hydraulic system has a low weight to power ratio compared to electromechanical systems. Fluid power systems are compact.
8) Fluid power systems can be used where safety is of vital importance: Safety is of vital importance in air and space travel, in the production and operation of motor vehicles, in mining and manufacture of delicate products

## Slide 14: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
APPLICATIONS OF FLUID POWER:
1) Agriculture: Tractors and farm equipments like ploughs, movers, chemical sprayers, fertilizer spreaders.
2) Aviation: Fluid power equipments like landing wheels on aeroplane and helicopter, aircraft trolleys, aircraft engine test beds.
3) Building Industry: For metering and mixing of concrete ingredients from hopper.
4) Construction Equipment: Earthmoving equipments like excavators, bucket loaders, dozers, crawlers, and road graders.
5) Defence: Missile-launch systems and Navigation controls
6) Entertainment: Amusement park entertainment rides like roller coasters
7) Fabrication Industry: Hand tools like pneumatic drills, grinders, bores, riveting machines, nut runners
8) Food and Beverage: All types of food processing equipment, wrapping, bottling
9) Foundry: Full and semi-automatic moulding machines, tilting of furnaces, die casting machines
10) Material Handling: Jacks, Hosts, Cranes, Forklift, Conveyor system

## Slide 15: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
PASCAL’S LAW (MULTIPLICATION OF FORCE):
Pascal’s law reveals the basic principle of how fluid power systems perform useful work. This law can be stated as follows:
Pressure applied to a confined fluid is transmitted undiminished in all directions throughout the fluid and acts perpendicular to the surface in contact with the fluid.

## Slide 16: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
DIFFERENT TYPES OF HYDRAULIC FLUIDS:
1) Water: The least expensive hydraulic fluid is water. Water is treated with chemicals before being used in a fluid power system. This treatment removes undesirable contaminates.
2) Petroleum Oils: These are the most common among the hydraulic fluids which are used in a wide range of hydraulic applications. The characteristic of petroleum based hydraulic oils are controlled by the type of crude oil used.
3) Water Glycols: These are solutions contains 35 to 55% water, glycol and water soluble thickener to improve viscosity. Additives are also added to improve anticorrosion, anti-wear and lubricity properties.
4) Water Oil Emulsions: These are water-oil mixtures. They are of two types’ oil-in-water emulsions or water-in-oil emulsions. The oil-in-water emulsion has water as the continuous base and the oil is present in lesser amounts as the dispersed media. In the water-in-oil emulsion, the oil is in continuous phase and water is the dispersed media.
5) Phosphate Ester: It results from the incorporation of phosphorus into organic molecules. They have high thermal stability. They serve an excellent detergent and prevent building up of sludge.

## Slide 17: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
PROPERTIES OF HYDRAULIC FLUIDS:
1) Viscosity: It is a measure of the fluid’s internal resistance offered to flow.
2) Viscosity Index: This value shows how temperature affects the viscosity of oil. The viscosity of the oil decreases with increase in temperature and vice versa. The rate of change of viscosity with temperature is indicated on an arbitrary scale called viscosity index.
3) Oxidation Stability: The most important property of hydraulic oil is its oxidation stability.
Oxidation is caused by a chemical reaction between the oxygen of the dissolved air and the oil. The oxidation of the oil creates impurities like sludge, insoluble gum and soluble acidic products. The soluble acidic products cause corrosion and insoluble products make the operation sluggish.
4) Demulsibility: The ability of a hydraulic fluid to separate rapidly from moisture and successfully resist emulsification is known as Demulsibility.
5) Lubricity: The ability of the hydraulic fluid to lubricate the moving parts efficiently is called Lubricity.
6) Rust Prevention: The moisture entering into the hydraulic system with air causes the parts made of ferrous materials to rust. This rust if passed through the precision made pumps and valves may scratch the nicely polished surfaces. So inhibitors are added to the oil to keep the moisture away from the surface.

## Slide 18: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
7) Pour Point: The temperature at which oil will clot is referred to as the pour point i.e. the lowest temperature at which the oil is able to flow easily.
8) Flash Point and Fire Point: Flash point is the temperature at which a liquid gives off vapor in sufficient quantity to ignite momentarily or flash when a flame is applied. The minimum temperature at which the hydraulic fluid will catch fire and continue burning is called fire point.
9) Neutralization Number: The neutralization number is a measure of the acidity or alkalinity of a hydraulic fluid. This is referred to the PH value of the fluid. High acidity causes the oxidation rate in an oil to increase rapidly.
10) Density: It is that quantity of matter contained in unit volume of the substance.
11) Compressibility: All fluids are compressible to some extent. Compressibility of a liquid causes the liquid to act much like a stiff spring. The coefficient of compressibility is the fractional change in a unit volume of liquid per unit change of pressure.
SELECTION OF HYDRAULIC FLUIDS:
A hydraulic fluid has the following four primary functions:
1) Transmit Power
2) Lubricate moving parts
3) Seal clearances between mating parts
4) Dissipate heat

## Slide 19: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
In addition a hydraulic fluid must be inexpensive and readily available. From the selection point of view, a hydraulic fluid should have the following properties:
1) Good lubricity
2) Ideal viscosity
3) Chemical stability
4) Compatibility with system materials
5) High degree of incompressibility
6) Fire resistance
7) Good heat-transfer capability
8) Low density
9) Foam resistance
10) Non-toxicity
11) Low volatility
This is a challenging list, and no single hydraulic fluid possesses all of these desirable characteristics. The fluid power designer must select the fluid that is the closest to being ideal overall for a particular application.

## Slide 20: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
PIPES AND HOSES:
In a hydraulic system, the fluid flows through a distribution system consisting of pipes (conductors) and fittings, which carry the fluid from the reservoir through operating components and back to the reservoir.
Hydraulic systems use primarily four types of conductors:
1. Steel pipes
2. Steel tubing
3. Plastic tubing
4. Flexible Hoses
The choice of which type of conductor to use depends primarily on the system’s operating pressures and flow-rates radial slot contains a vane, which is free to slide in or out of the slots due to centrifugal force. The cam ring axis is offset to the drive shaft axis. When the rotor rotates, the centrifugal force pushes the vanes out against the surface of the cam ring. The vanes divide the space between
QUICK ACTING COUPLINGS:
Couplings are precision components, engineered for specific uses with exact dimensions and close tolerances. There are a variety of applications in modern industrial plants for quick connect (QC) couplings both for pneumatically operated tools as well as other fluid power equipments which can be connected rapidly to their power source to permit wide versatility for production needs. For instance, in connecting or disconnecting a tractor and its hydraulically actuated agricultural component. QCs make changes simple, do not require additional hand tools, take little time and do not require the help of additional trade or skill. They are devices which permit the rapid connection or disconnection of fluid conductors

## Slide 21: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering
Fluid Power Symbols:

## Slide 22: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 23: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 24: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 25: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 26: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 27: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 28: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 29: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 30: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 31: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 32: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 33: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 34: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 35: Industrial Automation and Robotics
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 36: Summary
In this chapter, an introduction to the field of the automation and fluid power control was given and some significant to be noticed are given below;
Role of Automation in today’s world.
Fluid power control and the components used for devising a circuit.
education for life www.rimt.ac.in
Department of Mechanical Engineering

## Slide 37: Topics to be Discussed in Next Lecture
Basics Hydraulics and Pneumatic Circuits.
education for life www.rimt.ac.in
Department of Mechanical Engineering